## Slide 1
ARITHMETIC AND LOGIC UNIT

## Slide 2
Hardware implementation for Addition and Subtraction:

## Slide 3
Multiplication
UNSIGNED INTEGERS
Multiplicand (11) Multiplier (13) Product (143)
1011 X 1101
----------------
1011
0000
1011
1011
----------------------------
10001111

## Slide 7
TWOS COMPLEMENT MULTIPLICATION
Figure 9.10 Multiplication of Two Unsigned 4-Bit Integers Yielding an 8-Bit Result
(a) Unsigned integers
(b) Twos complement integers
Figure 9.11 Comparison of Multiplication of Unsigned and 2’s Complement Integers
1011 X 1101
----------------
1011
0000
1011
1011
----------------------------
10001111
Straightforward multiplication will not work if both the multiplicand and multiplier are negative.
In fact, it will not work if either the multiplicand or the multiplier is negative.

## Slide 8
Booth’s algorithm:
Adv: Benefit of speeding up the multiplication process, relative to a more straightforward approach.
The multiplier in Reg Q and multiplicand in M are placed.
There is a 1-bit register Q-1 placed logically to the right of the least significant bit of the Q register.
The results of the mul will appear in A & Q regs.
A and Q-1 are initialized to 0.

## Slide 10
Figure 9.12 Booth’s Algorithm for 2’s Complement Multiplication

## Slide 11
Consider a +ve multiplier 00011110 = 24 + 23 + 22 + 21 = 30
Is also equal to 25 – 21
The number of such operations can be reduced to two if we observe that
2n + 2n-1 + ...... + 2n-K = 2n+1 - 2n-K ----Eq 1
So the product can be generated by one addition and one subtraction of the multiplicand.
This scheme extends to any number of blocks of 1s in a multiplier.

## Slide 12
The same scheme works for a negative multiplier.
Let X be a negative number in twos complement notation. The leftmost bit of X is 1, because X is negative:
Then the value of X can be expressed as
Assume that the leftmost 0 is in the kth position. Thus, X is of the form
Then the value of X is
----2
From Equation (1), we can say that
Rearranging,
----3
Substituting Eqn 3 in eqn 2 we have
Look at page 324, how -6 is handled with above principle.

## Slide 13
DIVISION
Dividend = 147 Divisor = 11

## Slide 16
To deal with -ve numbers, we recognize that
D = Q * V + R
Here D – dividend V – Divisor Q – Quotient R – Remainder
Consider eg. of int div with all possible combinations of signs of D and V:
D = 7 V = 3 Q = 2 R = 1
D = 7 V = -3 Q = R =
D = -7 V = 3 Q = R =
D = -7 V = -3 Q = R =
Note that the signs of Q and R are easily derivable from the signs of D and V.
Specifically,
sign(R) = sign(D)
sign(Q) = sign(D) * sign(V)
Hence, 2’s complement division is
-to convert the operands into unsigned values and,
-at the end, to account for the signs by complementation where needed.
-2
1
-2
-1
2
-1