## Slide 2
AAA Instruction - ASCII Adjust after Addition
AAD Instruction - ASCII adjust before Division
AAM Instruction - ASCII adjust after Multiplication
AAS Instruction - ASCII Adjust for Subtraction

## Slide 3
AAA Instruction • AAA converts the result of the addition of two valid unpacked BCD digits to a valid 2-digit BCD number and takes the AL register as its implicit operand.
Two operands of the addition must have its lower 4 bits contain a number in the range from 0 - 9
The AAA instruction adjust AL so that it contains a correct BCD digit.
If the addition produce carry (AF=1), the AH register is incremented and the carry CF and auxiliary carry AF flags are set to 1.
If the addition did not produce a decimal carry, CF and AF are cleared to 0 and AH is not altered.
In both cases the higher 4 bits of AL are cleared to 0.

## Slide 4
Example - AAA •
MOV AH,0 ;Clear AH for MSD •
MOV AL,6 ;BCD 6 in AL
ADD AL,5 ;Add BCD 5 to digit in AL
AAA; AH=1, AL=1
MOV AH,0 ;Clear AH for MSD •
MOV AL,6 ;BCD 6 in AL
ADD AL,5 ;Add BCD 5 to digit in AL
DAA ;AL=11 representing BCD 11

## Slide 5
AAD Instruction • ADD converts unpacked BCD digits in the AH and AL register into a single binary number in the AX register in preparation for a division operation.
Before executing AAD, place the Most significant BCD digit in the AH register and Last significant in the AL register.
When AAD is executed, the two BCD digits are combined into a single binary number by setting AL=(AH*10)+AL and clearing AH to 0.
After the division AL will then contain the unpacked BCD quotient and AH will contain the unpacked BCD remainder

## Slide 6
Example - AAD
MOV AX,0205h ;The unpacked BCD number 25
AAD ;After AAD , AH=0 and AL=19h (25) •
Another Example ;
AX=0607 unpacked BCD for 67 decimal ;CH=09H
AAD ;Adjust to binary before division
AX=0043 = 43H =67 decimal
DIV CH ;Divide AX by unpacked BCD in CH ;AL = quotient = 07 unpacked BCD ;AH = remainder = 04 unpacked BCD

## Slide 7
AAM : ASCII Adjust after MultiplicationThis instruction, after execution, converts the product available In AL into unpacked BCD format.

## Slide 8
MOV AL, 04 ; AL = 04
MOV BL , 09 ; BL = 09
MUL BL ; AX = AL*BL ; AX=24H ;
AAM ; AH = 03, AL=06

## Slide 9
AAS : ASCII Adjust AL after Subtraction
This instruction corrects the result in AL register after subtracting two unpacked ASCII operands.
The result is in unpacked decimal format.
The procedure is similar to AAA instruction except for the subtraction of 06 from AL.

## Slide 10
NEG : NegateThe negate instruction forms 2’s complement of the specified destination in the instruction.
The destination can be a register or a memory location.
This instruction can be implemented by inverting each bit and adding 1 to it.
E.g. NEG ALAL = = 35H Replace number in AL with its 2’s complementAL = = CBH

## Slide 11
Flag Transfer Instructions LAHF:It copies the lower byte of flag register to AH.
E.g. LAHF
SAHF:It copies the contents of AH to lower byte of flag register.
E.g. SAHF

## Slide 12
Flag Transfer Instructions PUSHF:Pushes flag register to top of stack.
E.g. PUSHF
POPF:Pops the stack top to flag register.
E.g. POPF

## Slide 13: Logical instructions
SHR instruction: Shift Arithmetic Right
This instruction shifts the mentioned bits in the register to the right side one by one, but instead of inserting the zeroes from the left end, the MSB is restored.
The rightmost bit that is being
shifted is stored in the Carry Flag (CF)

## Slide 14
Syntax: SAR Register, Bits to be shifted Example: SAR BX, 5
Working: