## Slide 1: JMP instructions

## Slide 2
Program flow control
Controlling the program flow is a very important thing, this is where your program can make decisions according to certain conditions.
unconditional jumps The basic instruction that transfers control to another point in the program is JMP. The basic syntax of JMP instruction:
JMP label
To declare a label in your program, just type its name and add ":" to the end, label can be any character combination but it cannot start with a number, for example here are 3 legal label definitions:
label1: label2: a:
Label can be declared on a separate line or before any other instruction, for example:
x1: MOV AX, 1

## Slide 3: Jump instructions that test single flag
Instruction | Description | Condition | Opposite Instruction
JZ , JE | Jump if Zero (Equal). | ZF = 1 | JNZ, JNE
JC , JB, JNAE | Jump if Carry (Below, Not Above Equal). | CF = 1 | JNC, JNB, JAE
JS | Jump if Sign. | SF = 1 | JNS
JO | Jump if Overflow. | OF = 1 | JNO
JPE, JP | Jump if Parity Even. | PF = 1 | JPO
JNZ , JNE | Jump if Not Zero (Not Equal). | ZF = 0 | JZ, JE
JNC , JNB, JAE | Jump if Not Carry (Not Below, Above Equal). | CF = 0 | JC, JB, JNAE
JNS | Jump if Not Sign. | SF = 0 | JS
JNO | Jump if Not Overflow. | OF = 0 | JO
JPO, JNP | Jump if Parity Odd (No Parity). | PF = 0 | JPE, JP

## Slide 4: Jump instructions for signed numbers
Instruction | Description | Condition | Opposite Instruction
JE , JZ | Jump if Equal (=). Jump if Zero. | ZF = 1 | JNE, JNZ
JNE , JNZ | Jump if Not Equal (<>). Jump if Not Zero. | ZF = 0 | JE, JZ
JG , JNLE | Jump if Greater (>). Jump if Not Less or Equal (not <=). | ZF = 0 and SF = OF | JNG, JLE
JL , JNGE | Jump if Less (<). Jump if Not Greater or Equal (not >=). | SF <> OF | JNL, JGE
JGE , JNL | Jump if Greater or Equal (>=). Jump if Not Less (not <). | SF = OF | JNGE, JL
JLE , JNG | Jump if Less or Equal (<=). Jump if Not Greater (not >). | ZF = 1 or SF <> OF | JNLE, JG

## Slide 5: Jump instructions for unsigned numbers
nstruction | Description | Condition | Opposite Instruction
JE , JZ | Jump if Equal (=). Jump if Zero. | ZF = 1 | JNE, JNZ
JNE , JNZ | Jump if Not Equal (<>). Jump if Not Zero. | ZF = 0 | JE, JZ
JA , JNBE | Jump if Above (>). Jump if Not Below or Equal (not <=). | CF = 0 and ZF = 0 | JNA, JBE
JB , JNAE, JC | Jump if Below (<). Jump if Not Above or Equal (not >=). Jump if Carry. | CF = 1 | JNB, JAE, JNC
JAE , JNB, JNC | Jump if Above or Equal (>=). Jump if Not Below (not <). Jump if Not Carry. | CF = 0 | JNAE, JB
JBE , JNA | Jump if Below or Equal (<=). Jump if Not Above (not >). | CF = 1 or ZF = 1 | JNBE, JA

## Slide 6: loops
instruction | operation and jump condition | opposite instruction
LOOP | decrease cx, jump to label if cx not zero. | DEC CX and JCXZ
LOOPE | decrease cx, jump to label if cx not zero and equal (zf = 1). | LOOPNE
LOOPNE | decrease cx, jump to label if cx not zero and not equal (zf = 0). | LOOPE
LOOPNZ | decrease cx, jump to label if cx not zero and zf = 0. | LOOPZ
LOOPZ | decrease cx, jump to label if cx not zero and zf = 1. | LOOPNZ
JCXZ | jump to label if cx is zero. | OR CX, CX and JNZ
oops

## Slide 7
All conditional jumps have one big limitation, unlike JMP instruction they can only jump 127 bytes forward and 128 bytes backward (note that most instructions are assembled into 3 or more bytes). We can easily avoid this limitation using a cute trick: Get an opposite conditional jump instruction from the table above, make it jump to label_x.
Use JMP instruction to jump to desired location.
Define label_x: just after the JMP instruction.
label_x: - can be any valid label name, but there must not be two or more labels with the same name.

## Slide 8: CALL INSTRUCTION
This Instruction is used to transfer execution to a subprogram or procedure.
There are two basic types of CALL ’s : Near and Far.
Further Divided into:
Direct within-segment (near or intrasegment)
Indirect within-segment (near or intrasegment)
Direct to another segment (far or intersegment)
Indirect to another segment (far or intersegment)

## Slide 9
Near CALL Instruction •
A Near CALL is a call to a procedure which is in the same code segment as the CALL instruction .
When 8086 executes the near CALL instruction, it decrements the stack pointer by two and copies the offset of the next instruction after the CALL on the stack.
This offset saved on the stack is referred as the return address, because this is the address that execution will returns to after the procedure executes

## Slide 10
Near CALL Instruction
A near CALL instruction will also load the instruction pointer with the offset of the first instruction in the procedure.
A RET instruction at the end of the procedure will return execution to the instruction after the CALL by restoring the offset saved on the stack back to IP

## Slide 11
Far CALL Instruction •
Far CALL is a call to a procedure which is in a different segment that which contains the CALL instruction.
When 8086 executes the Far CALL instruction, it decrements the stack pointer by two and copies the content of CS register to the stack.
It then decrements the stack pointer by two again and copies the offset of the instruction after the CALL to the stack

## Slide 12
Far CALL Instruction •
Finally it loads CSR with segment base of the segment which contains the procedure and IP with the offset of the first instruction of the procedure in segment.
A RET instruction at end of procedure will return to the next instruction after the CALL by restoring the saved CS and IP from the stack.

## Slide 13
Example – Near CALL
Direct within-segment (near or intrasegment)
CALL MULTO
MULTO is the name of the procedure. The assembler determines displacement of MULTO from the instruction after the CALL and codes this displacement in as part of the instruction .
Indirect within-segment (near or intrasegment)
CALL BX •
BX contains the offset of the first instruction of the procedure .Replaces contents of IP with contents o register BX.

## Slide 14
Example – Far CALL
Direct to another segment (far or intersegment)
CALL SMART ;SMART is the name of the ;
Procedure
SMART PROC FAR ;Procedure must be declare as ;an far

## Slide 16: Procedures
Procedure is a part of code that can be called from your program in order to make some
specific task. Procedures make program more structural and easier to understand.
Generally procedure returns to the same point from where it was called. The syntax for procedure declaration:name PROC ; here goes the code ; of the procedure ... RET name ENDP

## Slide 17
name - is the procedure name, the same name should be in the top and the bottom, this is used to check correct closing of procedures. RET instruction is used to return to operating system. The same instruction is used to return from procedure (actually operating system sees your program as a special procedure).

## Slide 18
PROC and ENDP are compiler directives, so they are not assembled into any real machine code. Compiler just remembers the address of procedure. CALL instruction is used to call a procedure.

## Slide 19
CALL m1
MOV AX, 2
m1 PROC
MOV BX, 5
RET ; return to caller. m1 ENDP END
The above example calls procedure m1, does MOV BX, 5, and returns to the next instruction after CALL: MOV AX, 2.

## Slide 20
There are several ways to pass parameters to procedure, the easiest way to pass parameters is by using registers, here is another example of a procedure that receives two parameters in AL and BL registers, multiplies these parameters and returns the result in AX register:

## Slide 21
MOV AL, 1 MOV BL, 2 CALL m2 CALL m2 CALL m2 CALL m2 RET ; return to operating system. m2 PROC MUL BL ; AX = AL * BL. RET ; return to caller. m2 ENDP END

## Slide 22: MACRO
Macro is a set of instruction and the programmer can use it anywhere in the program by using its name. It is mainly used to achieve modular programming. So same set of instructions can be used multiple times when ever required by the help of macro. Wherever macro’s identifier is used, it is replaced by the actual defined instructions during compilation thereby no calling and return occurs.
Syntax of macro :
%macro macro_name number_of_parameters
<macro body>
%endmacro

## Slide 23
A Macro can be defined in a program using the following assembler directives: MACRO (used after the name of Macro before starting the body of the Macro) and ENDM (at the end of the Macro).
All the instructions that belong to the Macro lie within these two assembler directives.
And a call to Macro is made just by mentioning the name of the Macro:
Macro_name [ list of parameters]

## Slide 24
It is optional to pass the parameters in the Macro
f you want to pass them to your macros, you can simply mention them all in the very first statement of the Macro just after the directive: MACRO.
The advantage of using Macro is that it avoids the overhead time involved in calling and returning (as in the procedures)
Another advantage is that there is no need for accessing stack or providing any separate memory to it for storing and returning the address locations while shifting the processor controls in the program.

## Slide 25
But it should be noted that every time you call a macro, the assembler of the microprocessor places the entire set of Macro instructions in the mainline program from where the call to Macro is being made
This is known as Macro expansion

## Slide 26
MyMacro MACRO p1, p2, p3
MOV AX, p1
MOV BX, p2
MOV CX, p3
ENDM
ORG 100h
MyMacro 1, 2, 3
MyMacro 4, 5, DX
the above code is expanded into: MOV AX, 00001h MOV BX, 00002h MOV CX, 00003h MOV AX, 00004h MOV BX, 00005h MOV CX, DX

## Slide 27
Macros are expanded directly in code, therefore if there are labels inside the macro definition you may get "Duplicate declaration" error when macro is used for twice or more.
To avoid such problem, use LOCAL directive followed by names of variables, labels or procedure names.
For example:
MyMacro2 MACRO
LOCAL label1, label2
CMP AX, 2
JE label1
CMP AX, 3
JE label2
label1: INC AX
label2: ADD AX, 2
ENDM
ORG 100h
MyMacro2
MyMacro2

## Slide 28: Example macro
CODE SEGMENT
ASSUME CS:CODE
FACT MACRO
MOV BX,AX
DEC BX
BACK: MUL BX
DEC BX
JNZ BACK
ENDM
START: MOV AX,7
FACT
MOV AH,4CH
INT 21H
CODE ENDS
END START

## Slide 29
If you plan to use your macros in several programs, it may be a good idea to place all macros in a separate file. Place that file in Inc folder and use INCLUDE file-name directive to use macros

## Slide 30: procedure
Procedures are also like macro, but they are used for large set of instruction when macro is useful for small set of instructions. It contains a set of instructions which performs a specific task.
It contains three main parts i.e Procedure name to identify the procedure, procedure body which contains set of instructions, and RET statement which denotes return statement.
Unlike macros, procedures follow call-return method thereby achieving true modularity.

## Slide 31
S.No. | MACRO | PROCEDURE
01. | Macro definition contains a set of instruction to support modular programming. | Procedure contains a set of instructions which can be called repetitively which can perform a specific task.
02. | It is used for small set of instructions mostly less than ten instructions. | It is used for large set of instructions mostly more than ten instructions.
03. | In case of macro memory requirement is high. | In case of procedure memory requirement is less.
04. | CALL and RET instruction/statements are not required in macro. | CALL and RET instruction/statements are required in procedure.
05. | Assembler directive MACRO is used to define macro and assembler directive ENDM is used to indicate the body is over. | Assembler directive PROC is used to define procedure and assembler directive ENDP is used to indicate the body is over.
06. | Execution time of macro is less as it executes faster than procedure. | Execution time of procedures is high as it executes slower than macro.
07. | Here machine code is created multiple times as each time machine code is generated when macro is called. | Here machine code is created only once, it is generated only once when the procedure is defined.
08. | In a macro parameter is passed as part of statement that calls macro. | In a procedure parameters are passed in registers and memory locations of stack.
09. | Overhead time does not take place as there is no calling and returning. | Overhead time takes place during calling procedure and returning control to calling program.