## Slide 1: 8086 - Addressing modes
Click to add text

## Slide 3: Types of addressing modes
Addressing modes are the various methods used for accessing the data
Major categories:
  Immediate addressing
  Register addressing
  Memory addressing modes
    Direct addressing
    Indirect addressing
  I/O port addressing

## Slide 4
Brief explanation of MOV instruction to illustrate the addressing
  Performs data transfer
  MOV dest, src ; src is a source which can be a register, memory location or immediate data. Destn can be a register or memory location
  Src data size and dest location size must be same. For example: MOV AX,CL is invalid. MOV BH,CL is correct because both are 8 bits in size.

## Slide 5: 1. Immediate addressing
Source data is specified directly as a part of the instruction.
  Example:
  a. MOV AX, 1234H; AX = 1234H, i.e. AH= 12H and AL=34H
  b. MOV BL, 78H; BL=78H
  C. MOV CH, 4CH ; CH=4CH
  d. MOV DX, 4CH; DX= 004CH, i.e. DH =00H AND DL =4CH
  Destination register can also be SI, DI, BP but they can be used as only 16-bit registers. Eg: MOV SI, AX

## Slide 6: 2. Register addressing mode
Source and /or destination operand is specified in a register.
Operand is 8-bit or 16-bit
8-bit operand can Be: ?
16-bit operand can be:?
Segment registers (CS, DS, ES, SS) can also be used as 16-bit registers.
but segment registers are used to store most significant 16-bits of the base address of the respective segments.

## Slide 7: 2. Register addressing mode contd..
Examples:
Assume DX =1090H and DI= 34A0H;
MOV DX, DI ; DI= 34A0H AND DX= 34A0H
Assume DX =1090H
MOV CL, DH ; CL=?
Assume M is the symbolic memory location IN DATA segment; and BL=67H;
MOV M, BL; M=67H and BL=67H
Invalid instructions:
MOV AL,BX
MOV AX,CL

## Slide 8: 3. Memory addressing modes
Recall Physical address, Effective address /Offset
User data is always stored in the data segment of RAM and upper 16-bits of the base address of the data segment is stored in DS register.
20-bit physical address is calculated by BIU based on the displacement specified in the instruction.
The displacement in the instruction will be added to the DS register content unless it is specified to add to some other segment base.

## Slide 9: 3. Memory addressing modes contd..
Consider the following definition of the data segment
my_data segment
M1 db 12h ; define M1 as a byte
M2 dw 3456h ; define M2 as a word (16-bit)
my_data ends

## Slide 10: 3a. Direct memory addressing modes
The source or destination operand is provided by directly specifying the EA in the instruction itself.
Examples: Assume DS= 5672H, CX=9023H
  MOV BL ,M1 ; BL=?, physical address of M1 =?
  2. MOV M2, CX ;
  Content of M2 is ? Ans?
  MOV CL, DS:01H or MOV CL, [01H]; Assume the data segment definition of previous slide.
  4. MOV CX, DS:01H; Assume the data segment definition of previous slide.
Click to add text

## Slide 11: 3b-(i) Register indirect addressing mode.
EA is provided in the index register (SI or DI) or base register (only BX)
Assume SI= 0012H, DI=A142H, DS=5672h
1. MOV [SI], 567CH
Explanation:

## Slide 12: 3b. Indirect memory addressing modes
The EA of the operand is indirectly specified in one or two registers along with displacement value. Displacement value is optional in the instruction.
Five types of indirect addressing modes
  Register indirect
  Based addressing with displacement
  Indexed addressing with displacement
  Based Indexed addressing
  Based Indexed addressing with displacement

## Slide 13: 3b-(i) Register indirect addressing mode.
Assume BX= 89H, DI=A142H, DS=5672h
2. MOV DX, [BX]
Explanation:
Differentiate mov dx, si and mov dx, [si] with an example.

## Slide 14: 3b-(ii) Based addressing with displacement
Part of the EA is specified in the base registers(BX or BP) and other part (displacement) is directly provided in the instruction.
Displacement is a signed number and can be either positive or negative
Maximum size of the displacement is two bytes.
Negative displacement is represented in 2’s complement notation

## Slide 15: 3b-(ii) Based addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, BX=0189H
MOV 2[BX], 0BCA1H OR MOV [BX+2], 0BCA1H

## Slide 16: 3b-(ii) Based addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, BX=0189H
2. MOV -2[BX], 0BCA1H OR MOV [BX-2], 0BCA1H

## Slide 17: 3b-(ii) Based addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, BX=0189H
MOV 2[BX], 0A1H OR MOV [BX+2], 0A1H

## Slide 18: 3b-(ii) Based addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, BP=0189H
3. MOV 2[BP], 0BCA1H OR MOV [BP+2], 0BCA1H

## Slide 19: 3b-(iii) Indexed addressing with displacement
Part of the EA is specified in the index registers(SI or DI) and other part (displacement) is directly provided in the instruction.
Displacement is a signed number and can be either positive or negative
Maximum size of the displacement is two bytes.
Negative displacement is represented in 2’s complement notation

## Slide 20: 3b-(iii) Indexed addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, SI=0189H
MOV 2[SI], 0BCA1H OR MOV [SI+2], 0BCA1H

## Slide 21: 3b- (iii) Indexed addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, SI=0189H
2. MOV -2[SI], 0BCA1H OR MOV [SI-2], 0BCA1H

## Slide 22: 3b- (iv) Based Indexed addressing
Part of the EA is specified in the index registers(SI or DI) and other part is provided in the base register(BX,BP).

## Slide 23: 3b- (iv) Based Indexed addressing
Examples: Assume DS=5672H, SS= 8973H, SI=0189H, BX=1234H
MOV [SI][BX], 0BCA1H OR MOV [SI+BX], 0BCA1H

## Slide 24: 3b- (iv) Based Indexed addressing
Examples: Assume DS=5672H, SS= 8973H, DI=0189H, BP=4321H
2. MOV [DI][BP], 0BCA1H OR MOV [DI+BP], 0BCA1H

## Slide 25: 3b- (iv) Based Indexed addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, DI=0189H, BP=4321H
2. MOV 4[DI][BP], 0BCA1H OR MOV [DI+BP+4], 0BCA1H

## Slide 26: 3b- (v) Based Indexed addressing with displacement
Part of the EA is specified in the index registers(SI or DI) and other part is provided in the base register(BX,BP) and remaining part (displacement) is directly provided in the instruction.

## Slide 27: 3b- (v) Based Indexed addressing with displacement
Examples: Assume DS=5672H, SS= 8973H, SI=0189H, BX=1234H
MOV 2[SI][BX], 0BCA1H OR MOV [SI+BX+2], 0BCA1H

## Slide 28: 4. I/O port addressing
Processor does not directly communicate with I/O device.
It communicates with I/O ports which in turn communicates with I/O device.
I/O port is 8 bit and is outside microprocessor.
2 types of I/O port addressing mode:
Fixed port
Variable port
It's ok

## Slide 29: 4(a). Fixed port addressing
IN AL,83H
IN AX,83H

## Slide 30: 4(a). Fixed port addressing
OUT 83H,AL
OUT 83H,AX

## Slide 31: 4(b). Variable port addressing
OUT DX,AL
OUT DX,AX

## Slide 32: 4(b). Variable port addressing
IN AL,DX
IN AX,DX