## Slide 1
Few instructions of
8086 Microprocessor
Click to add text
Click to add text

## Slide 2
Mnemonic | Meaning | Format | Operation | Flags affected
MOV | Move | Mov D,S | (S)  (D) | None
Data Transfer Instructions - MOV
Destination | Source
Memory | Accumulator
Accumulator | Memory
Register | Register
Register | Memory
Memory | Register
Register | Immediate
Memory | Immediate
Seg reg | Reg 16
Seg reg | Mem 16
Reg 16 | Seg reg
Memory | Seg reg
NO MOV
Memory
Immediate
Segment Register
Memory
Segment Register
Segment Register
EX: MOV AL, BL

## Slide 3: Data Transfer Instructions - XCHG
Mnemonic | Meaning | Format | Operation | Flags affected
XCHG | Exchange | XCHG D,S | (S) (D) | None
Destination | Source
Accumulator | Reg 16
Memory | Register
Register | Register
Register | Memory
Example: XCHG [1234h], BX
NO XCHG
MEMs
SEG REGs

## Slide 4: Arithmetic Instructions: ADD, ADC, INC, AAA, DAA
Mnemonic | Meaning | Format | Operation | Flags affected
ADD | Addition | ADD D,S | (S)+(D)  (D) carry  (CF) | ALL
ADC | Add with carry | ADC D,S | (S)+(D)+(CF)  (D) carry  (CF) | ALL
INC | Increment by one | INC D | (D)+1  (D) | ALL but CF

## Slide 5: Arithmetic Instructions – SUB, SBB, DEC, AAS, DAS, NEG
Mnemonic | Meaning | Format | Operation | Flags affected
SUB | Subtract | SUB D,S | (D) - (S)  (D) Borrow  (CF) | All
SBB | Subtract with borrow | SBB D,S | (D) - (S) - (CF)  (D) | All
DEC | Decrement by one | DEC D | (D) - 1  (D) | All but CF
NEG | Negate | NEG D |  | All

## Slide 7: Multiplication and Division

## Slide 13
Click to add text

## Slide 16
Multiplication (MUL or IMUL) | Multiplicand | Operand (Multiplier) | Result
Byte*Byte | AL | Register or memory | AX
Word*Word | AX | Register or memory | DX :AX
Division (DIV or IDIV) | Dividend | Operand (Divisor) | Quotient: Remainder
Word/Byte | AX | Register or Memory | AL : AH
word/Word | DX:AX | Register or Memory | AX : DX
Multiplication and Division

## Slide 17
AAD: BCD-to-Binary Convert Before:
Converts 2 unpacked BCD digits in AH & AL to the equivalent binary number
In AL. [AL = (AH*10+AL); AH=00]
This adjustment must be made before dividing the two unpacked BCD digits in
AX by an unpacked BCD byte.
Assume AX = 0607H unpacked BCD for 67 decimal.
CH = 09
AAD ; AX=0043 = 43H=67 in Decimal
DIV CH ; Quotient AL = 07 unpacked BCD
; Remainder AH = 04 unpacked BCD

## Slide 18
AAM - BCD Adjust after Multiply:
After the two unpacked BCD digits are multiplied (i.e. byte multiplication), the AAM instruction is used to adjust product to two unpacked BCD digits in AX.
It works only on AL after multiplication.
ALTERNATIVELY, AH = Q(AL/10); AL = R(AL/10)
Assume
AL = 05 i.e. unpacked BCD 5
BH = 09 i.e. unpacked BCD 9
MUL BH ; AX = 2DH (45 in decimal)
AAM ; AX = 04 05H which is unpacked BCD for 45.
; If ASCII codes of the result are desired, use next
; instruction
OR AX, 3030H ; AX = 3435H

## Slide 19: Multiplication and Division Examples
Ex1: Assume that each instruction starts from these values:
AL = 85H, BL = 35H, AH = 0H
1. MUL BL → AL . BL = 85H * 35H = 1B89H → AX = 1B89H
2. IMUL BL → AL . BL = 2’S AL * BL = 2’S (85H) * 35H
= 7BH * 35H = 1977H→ 2’s comp → E689H → AX.
DIV BL → = = 02 (85-02*35=1B) →
4. IDIV BL → = =
1B | 
02
AH
AL
1B | 02
AH
AL
Click to add text

## Slide 20
Ex2: AL = F3H, BL = 91H, AH = 00H
MUL BL → AL * BL = F3H * 91H = 89A3H → AX = 89A3H
IMUL BL → AL * BL = 2’S AL * 2’S BL = 2’S (F3H) * 2’S(91H) =
0DH * 6FH = 05A3H → AX.
3.IDIV BL → = = = 2→ (00F3 – 2*6F=15H)
AH AL
15
02
R Q
→ 2’s(02) = FEH→
AH AL
15
FE
→
4. DIV BL → = = 01→(F3-1*91=62) →
AH AL
62
01
R Q

## Slide 21
Ex3: AX= F000H, BX= 9015H, DX= 0000H
1. MUL BX = F000H * 9015H =
DX AX
8713
B000
2. IMUL BX = 2’S(F000H) * 2’S(9015H) = 1000 * 6FEB =
DX AX
06FE
B000
3. DIV BL = = B6DH → More than FFH → Divide Error.

## Slide 22
Ex4: AX= 1250H, BL= 90H
1. IDIV BL → = = = = =
= 29H (Q) → (1250 – 29 * 70) = 60H (REM)
29H ( POS) → 2’S (29H) = D7H →
R Q
60H
D7H
2. DIV BL → = = 20H→1250-20*90 =50H →
R Q
50H
20H
AH AL

## Slide 23
Mnemonic | Meaning | Format | Operation | Flags Affected
AND OR XOR NOT | Logical AND Logical Inclusive OR Logical Exclusive OR LOGICAL NOT | AND D,S OR D,S XOR D,S NOT D | (S) · (D) → (D) (S)+(D) → (D) (D)→(D) _ (D) → (D) | OF, SF, ZF, PF, CF AF undefined OF, SF, ZF, PF, CF AF undefined OF, SF, ZF, PF, CF AF undefined None
+
Logical Instructions
Destination | Source
Register Register Memory Register Memory Accumulator | Register Memory Register Immediate Immediate Immediate
Destination
Register Memory

## Slide 24: LOGICAL Instructions
• AND
  – Uses any addressing mode except memory-to-memory and segment registers
  – Especially used in clearing certain bits (masking)
  xxxx xxxx AND 0000 1111 = 0000 xxxx
  (clear the first four bits)
  – Examples: AND BL, 0FH
  AND AL, [0345H]
• OR
  – Used in setting certain bits
xxxx xxxx OR 0000 1111 = xxxx 1111
(Set the upper four bits)

## Slide 25
XOR
    – Used in Inverting bits
    xxxx xxxx XOR 0000 1111 = xxxxx’x’x’x’
    -Example: Clear bits 0 and 1, set bits 6 and 7, invert bit 5 of register CL:
      AND CL, OFCH ; 1111 1100B
      OR CL, 0C0H ; 1100 0000B
      XOR CL, 020H ; 0010 0000B

## Slide 26
Shift and Rotate Instructions
SHR/SAL: shift logical left/shift
arithmetic left
SHR: shift logical right
SAR: shift arithmetic right
ROL: rotate left
ROR: rotate right
RCL: rotate left through carry
RCR: rotate right through carry

## Slide 27: Logical vs Arithmetic Shifts
A logical shift fills the newly created bit position with zero:
An arithmetic shift fills the newly created bit position with a copy of the number’s sign bit:

## Slide 28
Mnemo -nic | Meaning | Format | Operation | Flags Affected
SAL/SHL SHR SAR | Shift arithmetic Left/shift Logical left Shift logical right Shift arithmetic right | SAL/SHL D, Count SHR D, Count SAR D, Count | Shift the (D) left by the number of bit positions equal to count and fill the vacated bits positions on the right with zeros Shift the (D) right by the number of bit positions equal to count and fill the vacated bits positions on the left with zeros Shift the (D) right by the number of bit positions equal to count and fill the vacated bits positions on the left with the original most significant bit | CF,PF,SF,ZF AF undefined OF undefined if count ≠1 CF,PF,SF,ZF AF undefined OF undefined if count ≠1 CF,PF,SF,ZF AF undefined OF undefined if count ≠1
Shift Instructions

## Slide 29
Allowed operands
Destination | Count
Register Register Memory Memory | 1 CL 1 CL

## Slide 31: SHL Instruction
The SHL (shift left) instruction performs a logical left shift on the destination operand, filling the lowest bit with 0.
Operand types:
SHL reg,imm8
SHL mem,imm8
SHL reg,CL
SHL mem,CL

## Slide 32: Fast Multiplication
mov dl,5
shl dl,1
Shifting left 1 bit multiplies a number by 2
mov dl,5
shl dl,2 ; DL = 20
Shifting left n bits multiplies the operand by
2n
For example, 5 * 22 = 20

## Slide 33
Ex.
      SHL AX, 1
      MOV BX, AX
      MOV CL,2
      SHL AX,CL
      ADD AX, BX

## Slide 34: SHR Instruction
The SHR (shift right) instruction performs a logical right shift on the destination operand. The highest bit position is filled with a zero.
MOV DL,80
SHR DL,1 ; DL = 40
SHR DL,2 ; DL = 10
Shifting right n bits divides the operand by 2n

## Slide 35: SAR Instruction
SAR (shift arithmetic right) performs a right arithmetic shift on the destination operand.
An arithmetic shift preserves the number's sign.
MOV DL,-80
SAR DL,1 ; DL = -40
SAR DL,2 ; DL = -10

## Slide 36: Rotate Instructions
Mnem -onic | Meaning | Format | Operation | Flags Affected
ROL | Rotate Left | ROL D,Count | Rotate the (D) left by the number of bit positions equal to Count. Each bit shifted out from the left most bit goes back into the rightmost bit position. | CF OF undefined if count ≠ 1
ROR | Rotate Right | ROR D,Count | Rotate the (D) right by the number of bit positions equal to Count. Each bit shifted out from the rightmost bit goes back into the leftmost bit position. | CF OF undefined if count ≠ 1
RCL | Rotate Left through Carry | RCL D,Count | Same as ROL except carry is attached to (D) for rotation. | CF OF undefined if count ≠ 1
RCR | Rotate right through Carry | RCR D,Count | Same as ROR except carry is attached to (D) for rotation. | CF OF undefined if count ≠ 1

## Slide 37: ROL Instruction
ROL (rotate) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
MOV Al,11110000b
ROL Al,1 ; AL = 11100001b
MOV Dl,3Fh
ROL Dl,4 ; DL = F3h

## Slide 38: ROR Instruction
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the highest bit
No bits are lost
MOV AL,11110000b
ROR AL,1 ; AL = 01111000b
MOV DL,3Fh
ROR DL,4 ; DL = F3h

## Slide 39: RCL Instruction
RCL (rotate carry left) shifts each bit to the left
Copies the Carry flag to the least significant bit
Copies the most significant bit to the Carry flag
CLC ; CF = 0
MOV BL,88H ; CF,BL = 0 10001000b
RCL BL,1 ; CF,BL = 1 00010000b
RCL BL,1 ; CF,BL = 0 00100001b

## Slide 40: RCR Instruction
RCR (rotate carry right) shifts each bit to the right
Copies the Carry flag to the most significant bit
Copies the least significant bit to the Carry flag
STC ; CF = 1
MOV AH,10H ; CF,AH = 00010000 1
RCR AH,1 ; CF,AH = 10001000 0

## Slide 41
Destination | Count
Register Register Memory Memory | 1 CL 1 CL
Rotate Instructions

## Slide 43: LEA
loads any 16-bit register with the address, as determined by the addressing mode selected for the instruction
LEA AX, NUMB ; Loads AX with the address of NUMB
Note:
Operand address NUMB is loaded into register AX, not the contents of address NUMB
2. LEA BX, [DI] loads the offset address specified by [DI] (contents of DI) into the BX register; MOV BX, [DI] loads the data stored at the memory location addressed by [DI] into register BX
MOV BX, OFFSET LIST performs the same function as LEA BX, LIST.

## Slide 44: RAVI IS God
LDS and LES:
load any 16-bit register with an offset address, and the DS or ES segment register with a segment address.
use any of the memory-addressing modes to access a 32-bit section (containing a 16-bit offset and segment address) of memory.
E.g. LDS BX, [DI] instruction transfers the 32-bit number, addressed by DI in the data segment, into the BX and DS registers.
DD directive

## Slide 45: XLAT (translate)
converts the contents of the AL register into a number stored in a memory table.
performs the direct table lookup technique often used to convert one code to another.
first adds the contents of AL to BX to form a memory address within the data segment; then copies the contents of this address into AL.
Only instruction that adds an 8-bit number to a 16-bit number

## Slide 46
;Using an XLAT to convert from BCD to 7-segment code
DATA SEGMENT
TABLE DB 3FH, 6, 5BH, 4FH ;7-segment lookup table
DB 66H, 6DH, 7DH, 27H
DB 7FH, 6FH
CODE7 DB ?
DATA ENDS
CODE SEGMENT
MOV AL, 4 ;load test data
MOV BX, OFFSET TABLE ;address lookup table
XLAT ;convert to 7-segment
MOV CODE7, AL ;save 7-segment code

## Slide 47: PUSH/POP:
You can push register, memory, segment register, and flags on to LIFO stack
E.g., PUSH BX, PUSH WORD PTR [BX], PUSH DS, PUSHF
POP CX, POP WORD PTR[BX+1], POP DS
Updates SP
Initializing the stack:
stack_seg segment stack
dw 40 dup(0)
stack_top label word ; give name to next location after last
; word in stack
stack_seg ends
In code segment,
mov ax, stack_seg
mov ss, ax
lea sp, stack_top ; ;initialize SP

## Slide 48: LAHF and SAHF
LAHF transfers the rightmost eight bits of the flag register into the AH register.
SAHF transfers the AH register into the rightmost eight bits of the flag register.

## Slide 49: String primitives

## Slide 50: String primitives

## Slide 51: REP Prefix – saves execution time
REP string-primitive (MOVS, LODS, or STOS)
Repeat string operation until CX=0
Termination condition: (CX) =0
REPE string-primitive (CMPS, SCAS)
REPZ string-primitive (CMPS, SCAS)
Repeat string operation while Equal(or Zero)
Termination condition: (CX) =0 or (ZF) = 0
REPNE string-primitive (CMPS, SCAS)
REPNZ string-primitive (CMPS, SCAS)
Repeat string operation while Not Equal(or Not Zero)
Termination condition: (CX) =0 or (ZF) = 1
Note: In all cases, (CX) ← (CX)-1 with each repetition