## Slide 1: 8255 - Programmable Peripheral Interface MODE 0 EXAMPLES

## Slide 2: Stepper motor interfaced to 8255 MODE 0
A
B
C
D
CDAB
0 0 1 1 3
1 0 0 1 9
1 1 0 0 C
0 1 1 0 6
33H, 99H, CCH, 66H
(Rotating right)
33H, 66H, CCH, 99H
(rotating left)

## Slide 3: Stepper motor interfaced to 8255 MODE 0
C
D
A
B

## Slide 4
STEP PROC
MOV AL,10000000B
OUT CMD,AL
MOV AL,POS
OR CX,CX
JZ DOWN1
JS DOWN
REPEAT: ROL AL,1
OUT PORTA,AL
CALL DELAY
LOOP REPEAT
JMP DOWN1
DOWN: AND CX,7FFFH
UP: ROR AL,1
OUT PORTA,AL
CALL DELAY
LOOP UP
DOWN1:MOV POS,AL
RET
STEP ENDP
Click to add text

## Slide 5: Key Matrix interfaced to 8255 mode 0
PortB Output
PortA Input
Kecode Col Row
00 01 01
11 11 0F

## Slide 6: Key Matrix interfaced to 8255 mode 0
KEYSCAN PROC
KEYSCAN1: MOV AL,90h
OUT CMD, AL
MOV BH,00000001B
MOV AH,0
MOV CX,4
UP: MOV AL,BH
OUT PORTB,AL
IN AL,PORTA
CMP AL,0
JNZ GETKEYCODE
SHL BH,1
ADD AH,4
LOOP UP
JMP KEYSCAN1
GETKEYCODE: RCR AL,1
JC EXIT1
ADD AH,01
JMP GETKEYCODE
EXIT1: MOV AL,AH
RET
KEYSCAN ENDP