## Slide 1: COUNTER PROGRAMS

## Slide 2: Assume that following procedure definitions are available
disp_bcd : procedure to display a 2-digit bcd number
disp_hex : procedure to display a 2-digit hex number
kbrd_bcd: procedure to read a 2-digit bcd number
Kbrd_hex : procedure to read a 2-digit HEX number
disp_macro : Macro to display a string using AH, 09h
Definition of delay procedure:
DELAY: MOV DI, 0FH
BK2: MOV SI, 6FFFH
BK1: DEC SI
JNZ BK1
DEC DI
JNZ BK2
RET
Note: All procedures must be defined between
Mov ah 4ch
Int 21h
….
..
..
..
..
Code ends
End start

## Slide 3: TO DISPLAY A 2-DIGIT HEX COUNTER TO COUNT FROM 00 TO FF H once.
Initialize BL register to 0, BL=0
Get the cursor to the beginning of the nextline,
using macro “disp_macro nxtline”, where nxtline is defined in the data segment as db 10,13,’$’
Display BL content using disp_hex procedure
Displayed number should be seen on the screen for some time, so call a delay procedure
Increment BL
6. MOV dl, 13; mov h, 02; int 21h
7. Check if BL=?, if not equal go back to step3, if equal terminate the process.

## Slide 4: TO DISPLAY A 2-DIGIT HEX COUNTER TO COUNT FROM 00 TO FF H once.
DISP_MACRO macro ARG
lea dx, ARG
MOV AH, 09
INT 21H
ENDM
DATA SEGMENT
S Db ‘2-DIGIT HEX COUNTER:’, 10, 13, ‘$’
CR DB 13, ’$’
DATA ENDS
CODE SEGMENT
ASSUME CS:CODE, DS;DATA
START: MOV AX, DATA
MOV DS,AX
MOV BL,00 ; COUNTER
DISP_MACRO S
BK: CALL DISP_HEX
CALL DELAY
DISP_MACRO CR
INC BL
JNZ BK
MOV AH, 4CH
INT 21H
DISP_HEX:.
. . RET
DELAY:
.
.
RET
CODE ENDS
END START

## Slide 5: TO DISPLAY A 2-DIGIT HEX COUNTER TO COUNT FROM 00 TO FF H CONTINUOUSLY until user presses the key.
DISP_MACRO macro ARG
lea dx, ARG
MOV AH, 09
INT 21H
ENDM
DATA SEGMENT
S Db ‘2-DIGIT HEX COUNTER:’, 10, 13, ‘$’
CR DB 13, ’$’
DATA ENDS
CODE SEGMENT
ASSUME CS:CODE, DS;DATA
START: MOV AX, DATA
MOV DS,AX
MOV BL,00 ; COUNTER
DISP_MACRO S
BK: CALL DISP_HEX
CALL DELAY
mov dl,0ffh
mov ah,06
int 21h
jnz exit
DISP_MACRO CR
INC BL
JMP BK
EXIT: MOV AH, 4CH
INT 21H
; DEFINE PROCEDURES HERE
CODE ENDS
END START

## Slide 6: TO DISPLAY A 2-DIGIT DECIMAL TO COUNT FROM 00 TO 99 CONTINUOUSLY until user presses the key.
MOV BL,00 ; COUNTER
DISP_MACRO S
BK: CALL DISP_BCD
CALL DELAY
mov dl,0ffh ; INTERRUPT TO DETECT KEY PRESS
mov ah,06
int 21h
jnz exit ; ZF=0, AL= ASCII VALUE OF THE PRESSED KEY, AL==‘H’
DISP_MACRO CR
MOV AL,BL
ADD AL,01
DAA
MOV BL,AL
JMP BK

## Slide 7: Additional programs
Modify these programs to display 2-digit hex/DECIMAL counters
  up
  down
  up/down: if user inputs ‘U’: count upwards, ‘D’: downwards, ‘X’: Exit

## Slide 8: Thank You