## Slide 1: Pin Diagram of 8086 Microprocessor

## Slide 3
8086 is a 40 pin IC
[1] [20] Vss is ground
[40] Vcc is +5V power supply
[19] Clock  for timing purpose. Clock is generated externally. Works at 5MHz.
[39, 2 – 16] AD15 to AD0  Address/data bus lines compose multiplexed address/data bus on the 8086. Contain address bits A15 – A0 when [25] ALE=1 and contain data D15 – D0 when ALE = 0
[35 – 38] A19 – A16/ S6 – S3  Address/Status bus bits are multiplexed to provide address signals A19 – A16 and also status bits S6 – S3.
S6  always 0 and S5  Condition of IF flag bit
S4 | S3 | Function
0 | 0 | ES
0 | 1 | SS
1 | 0 | CS [or I/O port Access]
1 | 1 | DS

## Slide 4
[17] NMI  Non – Maskable Interrupt. Vectored interrupt.
[18] INTR  Maskable Interrupt. Non Vectored interrupt.
[24]  made zero when 8086 is ready to service INTR interrupt.
[21] RESET  Made high for atleast 4 clock cycles, 8086 gets reset.
CS=FFFFH, IP = 0000H,
other segment register are made 0
Flag register = 0000H
[22] READY 

## Slide 5
[23]  Is an input that is tested for WAIT instruction.
If = 1, Waits till it becomes 0
external device makes = 0 to indicate co processor has finished its computation.
[32] =0, receive data from memory or I/O device.
[33] MN/  =1 for minimum mode
=0 for maximum mode
Minimum mode pins:
[24]
[25] ALE

## Slide 6
[26]  Data bus enable. Activates external data bus buffers
[27] DT/  Data Transmit/Receive.
= 1 Microprocessor is transmitting
= 0 Microprocessor is receiving
[28] M/  = 1 Memory
      = 0 I/O
[29]
[30] HLDA
[31] HOLD

## Slide 7
Maximum mode pins:
[28, 27, 26] ,
[30, 31] / , /  DMA during maximum mode operation.
[29]  lock peripherals off the system.
[24, 25]  Qs1 and Qs0 queue status
 |  |  | Function
0 | 0 | 0 | Interrupt Acknowledge
0 | 0 | 1 | Read I/O port
0 | 1 | 0 | Write I/O port
0 | 1 | 1 | Halt
1 | 0 | 0 | Access code
1 | 0 | 1 | Read memory
1 | 1 | 0 | Write memory
1 | 1 | 1 | Passive
 |  |  | Function
0 | 0 | 0 | Interrupt Acknowledge
0 | 0 | 1 | Read I/O port
0 | 1 | 0 | Write I/O port
0 | 1 | 1 | Halt
1 | 0 | 0 | Access code
1 | 0 | 1 | Read memory
1 | 1 | 0 | Write memory
1 | 1 | 1 | Passive

## Slide 8
QS1 | QS0 | Function
0 | 0 | Queue is idle
0 | 1 | First byte of opcode
1 | 0 | Queue is empty
1 | 1 | Subsequent byte of opcode
[24, 25]  Qs1 and Qs0 queue status

## Slide 9
/S7 
At T1 clock cycle microprocessor sends . In subsequent clock cycles, Microprocessor sends 0 on S7 as status information.
Following cases of memory accesses are encountered:
1. Accessing an even addressed byte
2. Accessing an odd addressed byte
3. Accessing an even addressed word
4. Accessing an odd addressed word

## Slide 10: `