## Slide 1: Introduction to Real Time Operating Systems
Topics:
Real time systems & characteristics
Types of Real time Operating Systems
Applications
Event & Taxonomy of the events
Misconceptions about Real time systems
By
Mrs. Anuradha Rao
E-mail: anuradha.rao@manipal.edu

## Slide 2: Overview of the Real Time operating system
Real Time Operating systems itself is a vast subject
Topics Covered will give a glimpse of RTOS
The outcomes of these topics : Students should be
1. Able to understand the fundamental concepts of real time operating systems
2. Apply the knowledge to understand modern operating system concepts
Reference Books and the materials attached will clear your concept along with the ppts
Most of the content has been collected from the reference books mentioned in the next slide and nptel videos by Dr. Rajib Mall – Author of the second reference book
https://freevideolectures.com/course/3049/real-time-systems/2
you can browse through other lectures using the same link for modules 3,4,5,6,8,9,10,13

## Slide 3: Reference Books
Phillip A Laplante, Seppo J Ovaska, Real time systems design and analysis 4(e), Wiley,2013
Rajib Mall, Real time systems: Theory and Practice 2(e), Pearson, 2009.
Jane Liu, Real time Systems, Pearson, 2000

## Slide 4: Definition: Real-Time System
A real-time system is a computer system that must satisfy bounded response-time constraints or risk severe consequences, including failure
A real-time system is one whose logical correctness is based on both the correctness of the outputs and their timeliness
Real time: It is a quantitative notion of time measured using a physical clock
Example: After some event occurs the corresponding action must be completed within 10msec
In contrast, a qualitative notion of time can be expressed using after, before sometime, eventually etc

## Slide 5: Characteristics
Real time:
At least tasks have real time constraints, e.g.,
deadlines
Correctness Criterion:
Results should be logically correct and also
within the stipulated time

## Slide 6: Characteristics
Time Constraints – deadlines associated with tasks
Embedded – physically embedded in its environment and often controls it
Safety Critical – it should be highly reliable and should not cause extensive damages if it fails
Concurrent – needs to respond to several independent events within very short and strict time bounds
Reactive – in which on-going interaction between the computer and the environment is maintained

## Slide 7: Definition: Failed System
A failed system is a system that cannot satisfy one or more of the requirements stipulated in the system requirements specification
Hence, rigorous specification of the system operating criteria, including timing constraints, is necessary

## Slide 8: Definition: Embedded System
An embedded system is a system containing one or more
computers (or processors) having a central role in the functionality of the system, but the system is not explicitly called a computer
A real-time system may be embedded or non -embedded
But it is always reactive - Task scheduling is driven by ongoing interaction with the environment
Support for : timing aspects, memory management, networking, interfacing of wide range of I/O devices, scheduling, power management

## Slide 9: Degrees of “Real-Time”
All practical systems are ultimately real-time systems
Even a batch-oriented system—for example, grade processing at the end of a semester—is real-time
Although the system may have response times of days, it must respond within a certain time
Even a word-processing program should respond to commands within a reasonable amount of time
Most of the literature refers to such systems as soft real-time systems

## Slide 10: Applications
Industrial Applications
Medical Applications
Telecommunication applications
Aerospace
Internet and multi media
Consumer electronics
Defense
Railway reservation system

## Slide 11: Soft, Hard, and Firm “Real-Time”
Definition: Soft Real-Time System
performance is degraded by failure to meet time constraints
Examples: Word processing commands
Definition: Hard Real-Time System
failure to meet time constraints leads to system failure
Examples: Airbag systems in car, emergency brakes in {car, trains, heavy machineries)
Definition: Firm Real-Time System
less occurrences of missing a deadline can be tolerated
Video player: some frames may be missed
Sound system: missing some bits is ok

## Slide 12: Why RTOS ?
An Embedded system responds to external inputs: If response is late, system fails
A General purpose operating system minimizes response time and ensures fairness
A Real time operating system help tasks meet their deadlines

## Slide 13: Taxonomy of Events
An event can be either synchronous or asynchronous
  Synchronous events are those that occur at predictable times in the flow-of-control
  Asynchronous events occur at unpredictable points in the
flow-of-control and are usually caused by external sources
Moreover, events can be periodic, aperiodic or sporadic
  A real-time clock that pulses regularly is a periodic event
  Events that do not occur at regular periods are called
Aperiodic [not recurring at regular intervals]
  Aperiodic events that tend to occur very infrequently are called sporadic (recurring in scattered and irregular or unpredictable instances)
Event
Any occurrence that causes the program counter to change non-sequentially is considered a change of flow-of-control, and thus called an event. For example decision block, invocation of procedures, methods etc

## Slide 14: Usual Misconceptions
Real-time systems are synonymous with “fast” systems
  Many (but not all) hard real-time systems deal with deadlines in the tens of milliseconds
There are universal, widely accepted methodologies for real-time systems specification and design
  There is still no methodology available that answers all of the challenges of real-time specification and design all the time and for all applications
There is no more a need to build a real-time operating system, because many commercial products exist
  Commercial solutions have certainly their place, but choosing when to use an off-the-shelf solution and choosing the right one are continuing challenges

## Slide 15: Summary
Introduction to Real Time systems
Types of Real time systems
Applications
Need of Real Time Operating systems
Taxonomy of events
Misconceptions
Reference: Lec1_RTS.pdf sent