## Slide 1: ICT 2256: COMPUTER ORGANIZATION AND MICROPROCESSOR SYSTEMS [3 credit]
Dr. Rashmi Naveen Raj (rashmi.naveen@manipal.edu)
Dr. Santhosh Kamath (Santosh.kamath@maipal.edu)
Mrs. Divya Sharma (divya.sharma @manipal.edu)

## Slide 2: Syllabus:
Microprocessor 8086 Architecture, Pin diagram, Modes of operation, Segmentation and memory addressing, Addressing modes, Assembler directives, Assembly language development tools, Instruction set, Stacks and subroutine, Macros and procedures, Assembly language programming, Interrupts, BIOS and DOS interrupts, Basic IO interfacing- 8255 Programmable Peripheral Interface, 8254 Programmable Interval Timer, 8259 Programmable Interrupt Counter, Computer Organization: Introduction, Execution Unit - Combinational shifter design, Adders, Arithmetic and Logic Unit design, Multiplication algorithms, Division algorithms., Control Unit- Introduction, Basic concepts, Hardwired and Micro programming approach, Memory Unit, Input & Output.

## Slide 3: Course Outcomes:
Recall 8086 architecture
Write assembly language programs using development tools
Understand the interfacing of programmable devices to 8086 microprocessor
Understand the organisation of various parts in computer system
Design building blocks of computer system

## Slide 4: References:
Hall D.V., Microprocessors and Interfacing: Programming and Hardware (3e), Tata McGraw Hill, 2017, ISBN-10: 9781259006159
Brey B.B., The Intel Microprocessors: 8086 to Pentium Pro - Architecture, Programming and Interfacing (8e), Prentice Hall of India, 2012
Udaykumar K, Umashankar B.S., Advanced microprocessors and IBM –PC assembly language programming, McGraw Hill Education, 2017.
Rafiquzzaman M and Rajan C., Modern computer Architecture, Galgotia Publications Pvt. Ltd, 2012.

## Slide 5: What is a microprocessor?

## Slide 10: Few manufacturers
AMD
Mitsubishi
NEC
OKI
Toshiba
Siemens

## Slide 11: Basic elements of Microprocessor
To perform an operation microprocessor requires:
Registers
Arithmetic and Logic Unit (ALU)
Control Logic
Instruction register
Program counter
Bus
Click to add text
Click to add text

## Slide 12: Basic elements of Microprocessor

## Slide 13: Basic elements of Microprocessor

## Slide 14: 8086 Microprocessor : Features

## Slide 15: 8086 Microprocessor : Features

## Slide 16: Internal architecture of 8086

## Slide 17: Internal architecture of 8086

## Slide 18: 8086 Microprocessor: Architecture
Two main parts:
1. Bus interface unit
2. Execution Unit

## Slide 19: 8086 Microprocessor :Execution Unit
16-bit ALU
Control system and Instruction decoder
8 16-bit registers:
  Four 16-bit general purpose registers (AX (Accumulator), BX, CX, DX)
  OR (4x2)=8 8-bit general purpose registers (AH, AL, BH, BL, CH, CL, DH, DL)
  Four 16-bit special purpose registers
    SP – Stack Pointer
    BP – Base Pointer
    SI – Source Index
    DI - Destination Index
16-bit flag register
Click to add text

## Slide 20: 8086 Microprocessor : Flag register

## Slide 21: Carry flag

## Slide 22: Auxiliary Carry Flag

## Slide 23: Zero Flag

## Slide 24: Parity Flag

## Slide 25: Sign Flag

## Slide 26: Overflow Flag

## Slide 27
Control Flags
Direction Flag
Interrupt Flag
Trap Flag

## Slide 28: Direction Flag

## Slide 29: Interrupt Flag

## Slide 30: Trap Flag

## Slide 31: 8086 Microprocessor : Bus Interface Unit
Segment Registers
Instruction Queue
Instruction Pointer

## Slide 32: Need of Segmentation in 8086

## Slide 33: Segmentation in 8086

## Slide 34: 8086 Microprocessor : Bus Interface Unit
Segment Registers:
  Extra Segment (ES)
  Code Segment (CS)
  Stack Segment (SS)
  Data Segment (DS)

## Slide 35
20 – bit physical address generation