## Slide 1: Priority Inversion and Priority inheritance protocol

## Slide 2: Priority inversion
Higher priority task is blocked by a lower priority one.
May be caused by semaphore usage, device conflicts, bad design of interrupt handlers, poor programming and system design.

## Slide 3: A typical priority-inversion scenario
Blocked
Normal Execution
Critical Section




t0 t1 t2 t3 t4
t5 t6
t7 t8 Time

## Slide 4: Priority inheritance protocol
A solution to the priority inversion problem such that when a task blocks one or more higher-priority tasks, it temporarily inherits the highest priority of the blocked tasks.
The highest-priority task T1 relinquishes the processor whenever it seeks to lock the semaphore guarding a critical section that is already locked by some other job.
If a task T1 is blocked by T2 and , (i.e. has precedence over ) task T2 inherits the priority of T1 as long as it blocks T1. When T2 exits the critical section that caused the block, it reverts to the priority it had when it entered that section.
Priority inheritance is transitive. If T3 blocks T2, which blocks T1, then T3 inherits the priority of T1 via T2.

## Slide 5: Illustration of the priority- inheritance protocol
Blocked
Normal Execution
Critical Section




t0 t1 t2 t3 t4 t5
t6
t7 t8 Time
Priority Inherited
Priority Reverted

## Slide 6: Priority inheritance protocol
Priority inversion occurred in 1997 in NASA’s Mars Pathfinder Space
mission’s Sojourner rover vehicle.
Mil-std-1553B information bus manager was synchronized with semaphores.
A meteorological data gathering task that was of low priority and low frequency blocked a communications task that was of higher priority and higher frequency.
This infrequent scenario caused the system to reset.
The problem would have been avoided if the priority inheritance mechanism had been used. But it had been disabled.
Fortunately, the problem was diagnosed in ground based testing and remotely corrected by re-enabling the priority inheritance mechanism

## Slide 7: Priority ceiling protocol
The Priority Ceiling Protocol extends the Priority Inheritance Protocol through chained blocking in such a way that no task can enter a critical section in a way that leads to blocking it.
Each resource is assigned a priority (the priority ceiling) equal to the priority of the highest priority task that can use it.
The Priority Ceiling Protocol is the same as the Priority Inheritance Protocol, except that a task, T, can also be blocked from entering a critical section if there exists any semaphore currently held by some other task whose priority ceiling is greater than or equal to the priority of T.

## Slide 8: Illustration of the priority-ceiling protocol



t0 t1 t2 t3
t4
t5 t6
Acquire S2
Attempt to Acquire S1
Acquire S1

Acquire S2
Acquire S1
t7 t8 t9 Time

## Slide 9: Summary
What is Priority Inversion
Illustration of Priority inversion
Need of Priority inheritance
Priority Inheritance protocol
Illustration
Draw backs of Priority inheritance protocol
Priority Ceiling Protocol and Illustration
Ref: https://youtu.be/lFpYEaXHV5A