## Slide 1: Scrambling
Use scrambling to replace sequences that would produce constant voltage
Filling sequence
  Must produce enough transitions to sync
  Must be recognized by receiver and replace with original
  Same length as original
No dc component
No long sequences of zero level line signal
No reduction in data rate
Error detection capability

## Slide 2: B8ZS
Bipolar With 8 Zeros Substitution
Based on bipolar-AMI
If octet of all zeros and last voltage pulse preceding was positive encode as 000+-0-+
If octet of all zeros and last voltage pulse preceding was negative encode as 000-+0+-
Causes two violations of AMI code
Unlikely to occur as a result of noise
Receiver detects and interprets as octet of all zeros

## Slide 3: HDB3
High Density Bipolar 3 Zeros
Based on bipolar-AMI
String of four zeros replaced with one or two pulses

## Slide 4: HDB3 Rules

## Slide 5: B8ZS and HDB3

## Slide 6: Digital data, Analog signals

## Slide 7: Binary amplitude shift keying

## Slide 8: Binary amplitude shift keying

## Slide 9: Implementation of binary ASK

## Slide 10: Binary frequency shift keying
f1
f2

## Slide 11: Multiple FSK (MFSK)
More than two frequencies (M frequencies) are used
More bandwidth efficient compared to BFSK
More susceptible to noise compared to BFSK

## Slide 12
MFSK signal:
11
00
10
01
L=2
M=4
Ts
Minimum frequency separation 2fd=1/Ts
2fd
Bandwidth=2Mfd=M/Ts
Notes: Refer slide 17 the Gap between the lines(frequencies )must be 2fd

## Slide 13
MFSK signal:
Period of signal element
Minimum frequency separation
MFSK signal bandwidth:

## Slide 14
MFSK frequency use

## Slide 15: Example
Given a bandwidth of 10,000 Hz (1000 to 11,000 Hz), draw the full-duplex FSK diagram of the system. Find the carriers and the bandwidths in each direction. Assume there is no gap between the bands in the two directions.

## Slide 16
For full-duplex FSK, the bandwidth for each direction is
BW = 10000 / 2 = 5000 Hz
The carrier frequencies can be chosen at the middle of each band
fc (backward) = 1000 + 5000/2 = 3500 Hz
fc (forward) = 11000 – 5000/2 = 8500 Hz

## Slide 17: Example
With fc=250KHz, fd=25KHz, and M=8 (L=3 bits), we have the following frequency assignment for each of the 8 possible 3-bit data combinations: Find BW and data rate.

## Slide 18
This scheme can support a data rate of:

## Slide 19: Example
We need to send data 3 bits at a time at a bit rate of 3 Mbps. The carrier frequency is 10 MHz. Calculate the number of levels (different frequencies), the baud rate, and the bandwidth.

## Slide 20
We can have L=3,M = 23 = 8.
The baud rate is D=R/L
D= 3 Mbps/3 = 1 Mbaud.
The bandwidth is :
Tb=Bit period=1/3 micro sec
TS=LTb=3*(1/3) =1 micro sec
2fd=1/TS =1MHz
Bandwidth=8MHz
Tb=Ts/L
Ts=1/Baud Rate

## Slide 22: Phase Shift Keying

## Slide 24
Phase of the carrier is varied to represent digital data (binary 0 or 1)
Amplitude and frequency remains constant.
If phase 0 deg to represent 0, 180 deg to represent 1. (2level-PSK)
PSK is not susceptible to noise degradation that affects ASK or bandwidth limitations of FSK.

## Slide 25: Differential PSK (DPSK)
In DPSK, the phase shift is with reference to the previous bit transmitted rather than to some constant reference signal
Binary 0:signal burst with the same phase as the previous one
Binary 1:signal burst of opposite phase to the preceding one

## Slide 26: 4-PSK (Quadrature PSK) method

## Slide 28: Quadrature PSK
To increase the bit rate, we can code 2 or more bits onto one signal element.
In QPSK, we parallelize the bit stream so that every two incoming bits are split up and PSK a carrier frequency. One carrier frequency is phase shifted 90o from the other - in quadrature.
The two PSKed signals are then added to produce one of 4 signal elements. L = 4

## Slide 30: QPSK and Offset QPSK (OQPSK) Modulators

## Slide 32
Transmission bandwidth BT for ASK, PSK and FSK is of the form
  BT =(1+r)R
  R- Bit rate
  r- Related to technique typically 0<r<1

## Slide 33: Performance
Bandwidth Efficiency
  ASK/PSK/FSK:

## Slide 34: Example
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What should be the carrier frequency and the bit rate if we modulated our data by using FSK with r = 1?

## Slide 35
The midpoint of the band is at 250 kHz. B=100KHz, r=1
  BT=(1+r)R
  100=2R
  R=100/2=50kbps

## Slide 36: Example
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulate our data by using ASK with r= 1
BT=(1+r)R

## Slide 37: Quadrature Amplitude Modulation (QAM)
QAM used on asymmetric digital subscriber line (ADSL) and some wireless standards
combination of ASK and PSK
logical extension of QPSK
send two different signals simultaneously on same carrier frequency
  use two copies of carrier, one shifted by 90°
  each carrier is ASK modulated

## Slide 38: QAM modulator

## Slide 39: Tutorial
1. The waveform of Figure belongs to a Manchester encoded binary data stream. Determine the beginning and end of bit periods (i.e., extract clock information) and give the data sequence.
2. The bipolar-AMI waveform representing the binary sequence 0100101011 is
transmitted over a noisy channel. The received waveform is shown in Figure it contains a single error. Locate the position of this error and explain your answer.

## Slide 40
1.

## Slide 41
2. The error is at bit position 7, where there is a negative pulse. For AMI, positive and negative pulses are used alternately for binary 1. The pulse in position 1 represents the third binary 1 in the data stream and should have a positive value.

## Slide 42
3. One positive side effect of bipolar encoding is that a bipolar violation (two consecutive + pulses or two consecutive - pulses separated by any number of zeros) indicates to the receiver that an error has occurred in transmission. Unfortunately, upon the receipt of such a violation, the receiver does not know which bit is in error (only that an error has occurred). For the received bipolar sequence + - 0 + - 0 - + which has one bipolar violation, construct two scenarios (each of which involves a different transmitted bit stream with one transmitted bit being converted via an error) that will produce this same received bit pattern.

## Slide 43
3.
+-0+-0-+
a. +-0+-+-+
b. +-0+00-+
c. +-0+-00+

## Slide 44
Assume that a telephone line channel is equalized to allow bandpass data transmission over a frequency range of 600 to 3000 Hz. The available bandwidth is 2400 Hz. For r=1, evaluate the required bandwidth for 2400 bps QPSK