## Slide 1: Shannon Capacity
Shannon capacity: C = B log2 (1 + SNR)
Tradeoffs:
Increase bandwidth or signal power, increases data rate
Increase of noise, reduces data rate
Increase bandwidth, allows more noise
Increase signal power, causes increased intermodulation noise
› With noise, some bits may be corrupted; higher data rate, more bits corrupted
› Increasing signal strength overcomes noise
› Signal-to-noise ratio:
SNR =
signalpower
noisepower
High SNR high-quality signal  less intermediate repeaters

## Slide 2: Example of Shannon and Nyquist Capacity
A channel uses spectrum of between 3MHz and 4MHz, with SNRdB = 24dB. How many signal levels are required to achieve Shannon capacity?

## Slide 3: Example
A channel has B=4kHz and SNR =30dB. Determine maximum information rate for 128 level encoding.

## Slide 4: Solution
Nyquist capacity=56kbps
Shannon capacity=39.8kbps
Smallest of two values decide channel capacity.

## Slide 5: Example of Nyquist Capacity
A telephone system with modem allows bandwidth of 3100 Hz. What is the maximum data rate? M=2
If C=55800bps, what is M?