## Slide 1: Data Link Control Protocols Chapter 7

## Slide 8: Data Link Control Protocols
need layer of logic above Physical
to manage exchange of data over a link
  frame synchronization
  flow control
  error control
  addressing
  control and data
  link management

## Slide 9: Flow Control
ensure sending entity does not overwhelm receiving entity
  by preventing buffer overflow
influenced by:
  transmission time
    time taken to emit all bits into medium
  propagation time
    time for a bit to traverse the link
assume here no errors but varying delays

## Slide 10: Model of Frame Transmission
Vertical time sequence diagram

## Slide 11: Stop and Wait Flow control
source transmits frame
destination receives frame and replies with acknowledgement (ACK)
source waits for ACK before sending next frame
destination can stop flow by not sending ACK
works well for a few large frames
Stop and wait becomes inadequate if large block of data is split into small frames

## Slide 12: Stop and Wait Link Utilization

## Slide 13: Continued…
B = R . (d/V)
  B: length of the link in bits
  R: data rate of the link, in bps
  d: length or distance of the link in meters
  V: velocity of propagation, in m/s
a = B/L
  a: the propagation delay (with frame transmission time = 1)
  L: the number of bits in the frame
or

## Slide 14: Sliding Window Flow Control
allows multiple numbered frames to be in transit
receiver has buffer space of W frames long
transmitter sends up to W frames without ACK
ACK includes number of next frame expected
sequence number is bounded by size of field (k)
  frames are numbered modulo 2k
  giving max window size of up to 2k – 1
receiver can acknowledge frames without permitting further transmission (Receive Not Ready)
must send a normal acknowledge to resume
if we have full-duplex link, can piggyback ACKs

## Slide 15: Sliding Window Diagram

## Slide 16: Sliding Window Example

## Slide 17: Error Control
detection and correction of errors such as:
  lost frames
  damaged frames
common techniques for error control:
  error detection
  positive acknowledgment
  retransmission after timeout
  negative acknowledgement & retransmission

## Slide 18: Automatic Repeat Request (ARQ)
The effect of ARQ is to turn an unreliable data link into a reliable one. Three versions of ARQ are:
stop and wait ARQ
Go-back-N ARQ
Selective-reject ARQ (selective retransmission)

## Slide 19: Stop and Wait ARQ
source transmits single frame
wait for ACK
2 types of error occurs:
if received frame damaged, discard it
  transmitter has timeout
  if no ACK within timeout, retransmit. Source maintains a transmitted frame copy until ACK is received.
if ACK damaged, Transmitter will not recognize it
  transmitter will retransmit
  receive gets two copies of frame
  use alternate numbering and ACK0 / ACK1

## Slide 20: Stop and Wait ARQ
Advantage:
Simple

## Slide 21: Go-Back-N ARQ
based on sliding window
if no error, ACK as usual
if error, reply with rejection(REJ)
  discard that frame and all future frames until error frame received correctly.
  transmitter must go back and retransmit that frame and all subsequent frames

## Slide 22: Go-Back-N - Handling
Damaged Frame
  error in frame i so receiver rejects frame i .
  transmitter retransmits frames from i
Lost Frame
  frame i lost and either
    transmitter sends i+1 and receiver gets frame i+1 out of seq and rejects frame i (REJ i)
    or transmitter times out and send ACK with P bit set which receiver responds to with ACK i
  transmitter then retransmits frames from i

## Slide 23: Go Back N - Handling
Damaged Acknowledgement
  receiver gets frame i, sends ack (i+1) which is lost
  Ack’s are cumulative, so next ACK (i+n) may arrive before transmitter times out on frame i
  if transmitter times out, it sends ack with P bit set
  can be repeated a number of times before a reset procedure is initiated
Damaged Rejection
  reject for damaged frame is lost
  handled as for lost frame when transmitter times out

## Slide 24: Selective-Reject(ARQ)
only rejected frames are retransmitted
subsequent frames are accepted by the receiver and buffered
minimizes retransmission
receiver must maintain large enough buffer
more complex logic in transmitter
hence less widely used
useful for satellite links with long propagation delays

## Slide 25: Go-Back-N vs Selective-Reject

## Slide 26: Selective-reject ARQ
Window-size limitation
  E.g. 3 bit sequence number, window size = 7
  Station A sends frames 0 ~ 6 to station B
  Station B receives all seven frames and cumulatively acknowledges with RR7
  If RR 7 is lost
  A times out and retransmit frame 0

## Slide 27: Selective-reject ARQ (cont)
  B has already advanced its receive window to accept frames 7, 0, 1, 2, 3, 4, and 5. Thus, it assumes that frame 7 has been lost and that this is a new frame 0 which it accepts.
0 1 2 3 4 5 6 7 0 1 2 3 4 5 ...
S
R
RR7 lost
retx
Ö

## Slide 28: Selective-reject ARQ
Problem with the foregoing scenario
  overlay between the sending and receiving windows
Solution
  for a k-bit sequence number, the maximum window size is limited to 2k-1.
0 1 2 3 4 5 6 7 0 1 2 ...
S
R
RR4 lost
retx
x

## Slide 29: Stop and wait flow control performance issues

## Slide 30: Error free sliding window flow control
Window size W, transmission time = 1, propagation time = a
Case 1: W >= 2a + 1
  Sender A can transmit continuously with no pause and normalized throughput is 1.0
Case 2: W < 2a + 1
  Sender A exhausts its window at t = W and cannot send additional frames until t = 2a + 1.
  Normalized throughput is W / (2a+1)

## Slide 34: ARQ

## Slide 38
1. A channel has a data rate of 4 kbps and a propagation delay of 20ms. For what range of frame sizes does stop-and-wait give an efficiency of at least 50%?

## Slide 39: Consider the use of 1000-bit frames on a 1-Mbps satellite channel with a 270-ms delay. What is the maximum link utilization for: a. Stop-and-wait flow control? b. Continuous flow control with a window size of 7? c. Continuous flow control with a window size of 127? d. Continuous flow control with a window size of 255?

## Slide 40: High Level Data Link Control (HDLC)
an important data link control protocol
Defines
3 station types:
  Primary - controls operation of link
  Secondary - under control of primary station
  Combined - issues commands and responses
2 link configurations
  Unbalanced - 1 primary, multiple secondary. Supports full duplex and half duplex transmission.
  Balanced - 2 combined stations and supports full duplex and half duplex.

## Slide 41: Cont…
3 data Transfer Modes
Normal Response Mode (NRM)
  unbalanced configuration, primary initiates transfer
  used on multi-drop lines, many terminals are connected to host computer.
Asynchronous Balanced Mode (ABM)
  balanced configuration, either station initiates transmission without receiving permission from other combined station, has no polling overhead, widely used
Asynchronous Response Mode (ARM)
  unbalanced configuration, secondary may initiate transmit without permission from primary, primary holds responsibility for the line, rarely used

## Slide 42: HDLC Frame Structure
synchronous transmission of frames
single frame format used
Header
Trailer

## Slide 43: Flag Fields and Bit Stuffing
delimit frame at both ends with 01111110 seq
receiver hunts for flag sequence to synchronize
bit stuffing used to avoid confusion with data containing flag sequence 01111110
  0 inserted after every sequence of five 1s
  if receiver detects five 1s it checks next bit
  if next bit is 0, it is deleted (was stuffed bit)
  if next bit is 1 and seventh bit is 0, accept as flag
  if sixth and seventh bits 1, sender is indicating abort

## Slide 44: Address Field
identifies secondary station that sent or will receive frame
usually 8 bits long
may be extended to multiples of 7 bits
  Left most bit of each octet indicates if it is the last octet (1) or not (0)
all ones address 11111111 is broadcast

## Slide 45: Control Field
different for different frame type
  Information - data transmitted to user
    Flow and error control piggybacked on information frames
  Supervisory - ARQ when piggyback not used
  Unnumbered - supplementary link control
first 1-2 bits of control field identify frame type

## Slide 46: Control Field
use of Poll/Final bit depends on context
in command frame is P bit set to1 to solicit (poll) response from transmitter
in response frame is F bit set to 1 to indicate response to soliciting command
seq number usually 3 bits
  can extend to 8 bits as shown below

## Slide 47: Information & FCS Fields
Information Field
  in information and some unnumbered frames
  must contain integral number of octets
  variable length
Frame Check Sequence Field (FCS)
  used for error detection
  either 16 bit CRC or 32 bit CRC

## Slide 48: HDLC Operation
consists of exchange of information, supervisory and unnumbered frames
have three phases
  initialization
    by either side, set mode & seq
  data transfer
    with flow and error control
    using both I & S-frames (RR, RNR, REJ, SREJ)
  disconnect
    when requested or fault noted

## Slide 50: HDLC Operation Example

## Slide 51: HDLC Operation Example