## Slide 1: ECE 1051 : BASIC ELECTRONICS
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 2: Course Description
Part 1 : Analog Electronics
  Diodes and Applications
  BJT and Applications
  Operational Amplifiers
Part 2: Digital Electronics
  Number Systems and Codes
  Boolean Algebra
  Logic Gates
  Flipflops and Applications
Part 3: Principles of Electronic Communication
  Analog Communication
  Digital Communication
  Communication Networks
  Mobile Communication
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 3: Course Outcomes
At the end of this course, student will be able to:
CO1: Describe the characteristics of various electronic devices and analyze simple circuit applications using them.
CO2: Describe the working of rectifier, voltage regulator and R-C coupled amplifier.
CO3: Explain the concept of Op-Amp and its basic applications using suitable circuits.
CO4: Simplify Boolean expressions and implement simple digital circuits using logic gates.
CO5: Describe the principles of analog and digital communication.
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 4: References
Albert P Malvino, David J Bates – Electronic Principles,7th edition, TMH,2007
Robert L. Boylestad, Louis Nashelsky- Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012
Malvino and Leach- Digital Principles & applications, 7th edition, TMH, 2010.
Morris Mano- Digital design, Prentice Hall of India, Third Edition.
George Kennedy, Bernad Davis- Electronic Communication Systems, 4thedition, TMH, 2004.
Dennis Roddy & John Coolen , "Electronic Communications" ,4th edition, Pearson Education,2009
Garcia and Widjaja, “Communication Networks”, McGraw Hill, 2006
Raj Pandya, “Mobile and Personal Communication Services and Systems”, Wiley-IEEE Press, 1999
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 5: Part – I : Analog Electronics
CHAPTER-1: DIODES AND APPLICATONS
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 6: Module – 1 : Diodes
Learning outcomes
At the end of this module, students will be able to:
Explain the operation of PN junction diode under different biasing condition.
Draw the I-V characteristic of diode and differentiate between ideal and practical diodes
Explain the concept of static and dynamic resistance of the diode.
Explain various breakdown phenomenon observed in diodes.
Describe the working of Zener diode and its I-V characteristic.
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 7: Review
Basics of Semiconductors
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 8: Classification of Materials Based on Energy Band Theory
Department of Electronics and Communication Engineering, MIT, Manipal

## Slide 9: Semiconductors
The resistivity of a semiconductor is less than that of an insulator but more than that of a conductor
A semiconductor has negative temperature co-efficient of resistance
Conducting properties change appreciably by adding suitable impurities (e.g.,Arsenic,Gallium etc.,)-Doping

## Slide 10: Semiconductor Materials
Semiconducting materials
Crystal structure of silicon
Department of Electronics and Communication Engineering, MIT, Manipal
Common Semiconducting materials : Ge, Si, GaAs
Notes: A semiconductor is a material which has electrical conductivity between that of a conductor such as copper and that of an insulator such as glass. Semiconductors are the foundation of modern electronics, including transistors, solar cells, light-emitting diodes (LEDs), quantum dots and digital and analog integrated circuits.
Mostly used semiconductor material is silicon. It consists of silicon in which the crystal lattice of the entire solid is continuous, unbroken (with no grain boundaries) to its edges. Silicon atomic core is surrounded by four valence electrons.

## Slide 11: Semiconductor Materials
Single-crystal
  Silicon(14)
  Germanium (32)
Compound
  Gallium Arsenide

## Slide 12: Structure of Semiconductor Material

## Slide 13: Semiconductor Materials

## Slide 14: Intrinsic & Extrinsic Semiconductors
Intrinsic Semiconductors
  Semiconductors in pure form are intrinsic
  Free electrons are due to external causes (light/ temperature)
Extrinsic Semiconductors
  Subjected to doping
  Adding pentavalent impurity results n-type
  Adding trivalent impurity results p-type

## Slide 15: n-type Semiconductor
Pentavalent impurities (antimony, arsenic, phosphorous etc.) are added – Donor atoms
Electrons are majority carriers

## Slide 16: P-type semiconductor
Trivalent impurities (Boron, gallium, indium etc.) are added
Holes are majority carriers

## Slide 17: p-type and n-type materials

## Slide 18: P-N Junction Diode
P
N
Anode
Cathode
Common practical diodes available in market
Department of Electronics and Communication Engineering, MIT, Manipal
Notes: P-N Junction diode: is a 2-terminal, 2-layer, single-junction semiconductor device made out of a single block of silicon or germanium, with one side doped with acceptor (p-type) impurity and the other side with donor (n-type) impurity. Numerous applications are like Switch, Rectifier, Regulator, Voltage multiplier, Clipping, Clamping, etc.
Construction:
The two terminals are called Anode and Cathode
1.At the instant the two materials are “joined”, electrons and holes near the junction cross over and combine with each other
2.Holes cross from P-side to N-side
3.Free electrons cross from N-side to P-side
4.At P-side of junction, negative ions are formed
5.At N-side of junction, positive ions are formed

## Slide 19: P-N Junction Diode
Used in numerous applications
Switch,
Rectifier,
Regulator,
Voltage multiplier,
Clipping,
Clamping, etc.

## Slide 20: P-N Junction Diode under biasing
P-N junction (a) in contact (b) formation of depletion region
Notes: Notes:
A PN junction have
- A P-type and N-type region
- Depletion region - region having no free carriers
Further movement of electrons and holes across the junction stops due to formation of depletion region
- Depletion region acts as barrier opposing further diffusion of charge carriers. So diffusion stops within no time
- Current through the diode under no-bias condition is zero Bias.

## Slide 21: P-N Junction Diode
Unbias condition
Notes: In the absence of an applied bias voltage, the net flow of charge in any one direction for a semiconductor diode is zero. This occurs because any minority carriers (holes) in the n-type material that find themselves within the depletion region will pass directly into the p-type material. The same happens with due to the electrons in the depletion region that will pass to the n-type material. The result is a depletion region empty of charge carriers, with high impedance, so no net current passes through the diode. This results in development of built-in potential ranging from 0.3-0.7 eV depending upon the type semiconducting material used.

## Slide 22: Forward bias
Positive of battery connected to p-type (anode)
Negative of battery connected to n-type (cathode)
Diode under forward biasing conditions
Notes: Forward biasing:
When forward biasing is applied
-Electrons in n-type are forced to recombine with positive ions near the boundary, similarly holes in p-type are forced to recombine with negative ions
-Depletion region width reduces
-An electron in n-region “sees” a reduced barrier at the junction and strong attraction for positive potential
-As forward bias is increased, depletion region narrows down and finally disappears – leads to exponential rise in current
- Forward current is measured in milli amperes

## Slide 23: Forward Bias

## Slide 24: Reverse bias
Positive of battery connected to n-type material (cathode)
Negative of battery connected to p-type material (anode)
Diode under reverse biasing conditions
Notes: Reverse biasing:
When reverse bias is applied
-Free electrons in n-region are drawn towards positive of battery, Holes in p-region are drawn towards negative of battery
-Depletion region widens, barrier increases for the flow of majority carriers
-Majority charge carrier flow reduces to zero
-Minority charge carriers generated thermally can cross the junction – results in a current called “reverse saturation current”.

## Slide 25: Reverse bias

## Slide 26: I-V characteristic of practical diode
Vγ is 0.6 ~ 0.7 Vfor Si
0.2 ~ 0.3 V for Ge
(mA)
(μA)
Notes: I-V characteristics:
I-V characteristics of the practical diode. The forward current is in the range of milli amperes when forward biased. When the diode is reverse biased only reverse saturation current flows which is in the range of few micro amperes.

## Slide 27: Breakdown phenomenon in diodes
Two breakdown mechanisms:
  Avalanche breakdown :
  Occurs in Lightly doped diodes,
  Occurs at high reverse Voltage.
  Zener Breakdown:
  Occurs in heavily doped diodes.
  at lower reverse bias voltages.
Notes: Break down phenomenon in diodes:
Breakdown voltage is a parameter of a diode that defines the largest reverse voltage that can be applied without causing an exponential increase in the current in the diode. As long as the current is limited, exceeding the breakdown voltage of a diode does no harm to the diode.
Zener breakdown can be reversible (zener breakdown) and irreversible (avalanche breakdown) .
There are two breakdown mechanisms exist in diode.They are
-Zener breakdown
-Avalanche breakdown

## Slide 28: Avalanche Breakdown
Schematic of Avalanche phenomenon
Notes: Avalanche breakdown occurs when the applied voltage is so large that electrons that are pulled from their covalent bonds are accelerated to great velocities. These electrons collide with the silicon atoms and knock off more electrons. These electrons are then also accelerated and subsequently collide with other atoms. Each collision produces more electrons which leads to more collisions .The current in the semiconductor rapidly increases and the material can quickly be destroyed.Avalanche breakdown is observed for reverse bias voltages above 6V.

## Slide 29: Zener Breakdown
Schematic of Zener phenomenon
Notes: In Zener breakdown the electrostatic attraction between the negative electrons and a large positive voltage is so great that it pulls electrons out of their covalent bonds and away from their parent atoms. Electrons are transferred from the valence to the conduction band. In this situation, the current can still be limited by the limited number of free electrons produced by the applied voltage so it is possible to cause Zener breakdown without damaging the semiconductor.This breakdown is observed for reverse bias voltages below 4V.

## Slide 30: Silicon vs. Germanium

## Slide 31: Effect of Temperature on the Reverse current
I (mA)
V (volts)
I (μA)
–75oC
25oC
125oC

## Slide 32: Diode current equation
ID is diode current
Io is reverse saturation current
VD is voltage applied to diode (+ve for forward and –ve for reverse bias)
VT is thermal voltage = kT/q = T / 11600 (T is temperature in Kelvin = 273+temp in OC)
η is a constant = 1 for Ge and 2 for Si

## Slide 33: Diode current equation
For positive values of VD (forward bias),
For large negative values of VD (reverse bias), ID ≈ –Io

## Slide 34: Effect of Temperature on the Diode current
Reverse current doubles for every 10 degree rise in temperature.
Forward cut-in voltage changes -2.5mV/0C increase in temparature

## Slide 35: Problems
  Q1. A Si diode has reverse sat current 12nA at 20oC. (a) Find the diode current when it is forward biased by 0.65 V. (b) Find the diode current when the temperature rises to 100oC.
Ans:
ID1=4.644mA, ID2 = 75.2mA

## Slide 36: Problems
Q2. A Silicon diode has a saturation current of 1pA at 200C. Determine (a) Diode bias voltage when diode current is 3mA (b) Diode bias current when the temperature changes to 1000C, for the same bias voltage.
Notes: Effect of Temperature on the Reverse current:
-Cut-in voltage decreases with increase in temperature
Io1 is the reverse saturation current at temperature T1. If the temperature varies to T2, then I02 reverse saturation current at temperature T2
doubles for every 10 degree rise in temperature.

## Slide 37
Q2. A Silicon diode has a saturation current of 1pA at 200C. Determine (a) Diode bias voltage when diode current is 3mA (b) Diode bias current when the temperature changes to 1000C, for the same bias voltage.
Ans:
VD = 1.1 V, ID2 = 7.07mA
Notes: Effect of Temperature on the Reverse current:
-Cut-in voltage decreases with increase in temperature
Io1 is the reverse saturation current at temperature T1. If the temperature varies to T2, then I02 reverse saturation current at temperature T2
doubles for every 10 degree rise in temperature.

## Slide 38: Exercise Problems
  Q1. A silicon diode is reverse biased with 5V at room temperature. if reverse sat current is 60pA, what is the diode current? (Ans: -60pA)
  Q2. A germanium diode carries a current of 10mA when it is forward biased with
  0.2V at 27oC. (a) Find reverse sat current. (b) Find the bias voltage
  required to get a current of 100mA. (Ans:4.37μA,0.2854V)
  Q3. Calculate the factor by which reverse saturation current of silicon diode is
  multiplied when the temperature increases from 25 to 100OC. (Ans:181)
Q6. The forward current in a Si diode is 15 mA at 27oC. If reverse saturation current is 0.24nA, what is the forward bias voltage? (Ans: 0.98V)
Q7. A germanium diode carries a current of 10mA when it is forward biased with 0.2V at 27oC. (a) Find reverse sat current. (b) Find the bias voltage required to get a current of 100mA. (Ans:4.37μA,0.2854V)

## Slide 39: Diode resistances
Static or DC resistance:
  Ratio of diode voltage and diode current
  Lower the current through the diode, higher the DC resistance level
  The dc resistance at the knee and below will be greater than the resistance at the linear section of characteristic
  The dc resistance in the reverse bias region will naturally be quite high
Notes: DC resistance:
  -The dc resistance at the knee and below will be greater than the resistance at the linear section of characteristics.
  -The dc resistance in the reverse bias region will naturally be quite high.
Dynamic or AC resistance
  -Often sinusoidal voltages are applied to diode
  -So the instantaneous operating point moves up and down in the characteristic curve
  -So DC resistance is not a suitable parameter
  -Instead, AC resistance is used
  -It is the change in the diode voltage divided by the corresponding change in the diode current, where the change is as small as possible.
-Dynamic resistance can be found using previous equation, no need of characteristic curve
-Dynamic resistance in reverse region is very high, since slope of characteristic curve is almost zero
-The resistance calculated using equation does not include the resistance due to the metal contact (usually less than 0.1 Ω).

## Slide 40: Diode resistances
Determine the dc resistances at the three different operating points A, B and C.
Ans: RA= 40 ohms, RB=250 ohms, RC=10 M ohms

## Slide 41: Diode resistances
Dynamic or AC resistance
  When input is ac (varying)
  It is the change in the diode voltage divided by the corresponding change in the diode current, where the change is as small as possible

## Slide 42: Dynamic or AC resistance

## Slide 43: Diode resistances
AC resistance is nothing but reciprocal of the slope of the tangent line drawn at that point
AC resistance in reverse region is very high, since slope of characteristic curve is almost zero
Derivative of a function at a point is equal to the slope of the tangent line at that point

## Slide 44: Diode resistances
Determine the AC resistances at operating points A and B
Ans: rA=2 ohms, rB=25 ohms

## Slide 45: Problems
2. Find the static and dynamic resistance of a P-N junction germanium diode if the temperature is 27°C and I0=1μA for an applied forward bias of 0.2V.
Ans: ID=2.283mA, RD=87.6 Ohms, rD= 11.33 Ohms

## Slide 46: Exercises
3. Calculate the dynamic forward and reverse resistance of a P - N junction diode, when the applied voltage is 0.25V for Germanium Diode. I0 = lμA and T = 300 K.
(Ans:rf=1.637Ω;rr=2.586 MΩ)
  .

## Slide 47: Exercises
4. Calculate the dynamic forward and reverse resistance of a P - N junction diode, when the applied voltage is 0.2V for Germanium Diode. I0 = 30μA at a temperature 125oC.
(Ans: 3.356 ohms, 389.49kohms)

## Slide 48: Ideal Diode
Cut-in voltage is zero
No barrier potential. Small forward bias voltage causes conduction through the device
Forward resistance is zero
Reverse resistance is infinity
Conducts when forward biased and blocks conduction when reverse biased. Hence reverse saturation current is zero

## Slide 49: Ideal diode : I-V characteristics
I-V characteristic of Ideal diode and ideal models
Notes: Ideal Diode:
An ideal diode is simply a pn junction where the change from p-type to n-type material is assumed to occur instantaneously, also referred to as an abrupt junction. The simplified diode model ignores the effect of diode resistance in comparison with values of other elements of the circuit. The voltage drop across the diode (0.7 V for Si) is negligible. Hence the diode voltage drop can be ignored for simplification purpose.

## Slide 50: Practical Diode
For conduction, the barrier potential has to be overcome
Forward resistance is in the range of tens of ohms
Reverse resistance is in range of mega ohms
Does not conduct when reverse biased. However there is reverse saturation current flowing through the device

## Slide 51: Diode Equivalent Circuit
Used during circuit analysis
Characteristic curve replaced by straight-line segments (piecewise linear characteristics)

## Slide 52: Diode Equivalent Circuit
Forward bias
Reverse bias
Vγ
RF
A
K
A
K
A
K
Vγ
1/RF
RR = 

## Slide 53: Diode Equivalent Circuit
As second approximation, we can neglect the slope of the characteristic i.e., RF = 0 and
Vγ
A
K
A
K
A
K
Forward bias
Reverse bias
Vγ
RR = 
RF = 0
Vγ

## Slide 54: Diode Equivalent Circuit
As third approximation, even the cut-in voltage can be neglected (Ideal diode), RF = 0 and Vγ
Forward bias
Reverse bias
A
K
A
K
A
K
Vγ = 0
RR = 
RF = 0

## Slide 55: Self test
1. The arrow direction in the diode symbol indicates
a. Direction of electron flow.
b. Direction of hole flow (Direction of conventional current)
c. Opposite to the direction of hole flow
d. None of the above
2. When the diode is forward biased, it is equivalent to
a. An off switch b. An On switch
c. A high resistance d. None of the above
.

## Slide 56: Self test
1. The break-point voltage of Si diode is
a. 0.2V b. 0.7V c. 0.8V d. 1.0V
2. Why would you use silicon diodes instead of germanium diodes?

## Slide 57: Self test
1.Why silicon is preferred over germanium for semiconductor devices?
2.List different elemental and compound semiconductors.
Department of Electronics and Communication Engineering, MIT, Manipal