## Slide 1: Chapter 1: Diodes and Applications
Module – 2 : Applications of Diodes
Reference: Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuits Theory, 11th Edition, PHI, 2012

## Slide 2: At the end of this module, students will be able to:
Explain need for AC to DC conversion
Discuss basic DC power supply unit.
Discuss and analyze the working of a various rectifier circuits.
Explain how capacitor filter can be used to minimize the ac component.

## Slide 3: Topics
Introduction
Half wave rectifier
Full wave rectifier
  Center tapped FWR
  Full wave bridge rectifier
Rectifiers with capacitor filter

## Slide 4: Introduction
AC and DC signal
Electricity distribution in INDIA: AC signal of 230V, 50HZ.
AC signal with A=230V, f=50Hz

## Slide 5: Introduction
AC Signal
Define
Average/DC/mean value
RMS of effective value

## Slide 6: Introduction
Calculate the DC and RMS value of the signal

## Slide 7: Block diagram of a DC power supply

## Slide 8
Steps of conversion
Step down transformer
Regulator output (Pure DC)
Filtered output
Rectified output w.r.t. transformer output
Notes: A step down transformer reduces the voltage of an ac signal is called a step down transformer.
Rectifiers converts an ac sinusoidal signal that is bidirectional with positive and negative amplitudes into a signal with only unidirectional amplitudes that is only positive or only negative. Thus rectifier circuit forces the current through the load to flow in only in one direction. The out put of rectifier is called pulsating dc signal.
A filter circuit filters ac content from pulsating dc. A filter has to have a capacitor, an energy storing component that can hold the voltage to the peak value of the rectified pulsating dc and then dissipate energy to load when the pulsating dc drops.
Finally regulator is used to provide constant dc voltage despite of variations in the mains ac power supply or load variations.

## Slide 9: Rectifier
Converts AC to pulsating DC
Diode is the primary element
Half wave rectifier
Full wave rectifier
  Centre tapped full wave rectifier
  Full wave bridge rectifier

## Slide 10: Half wave rectifier

## Slide 11: Working of HWR
Equivalent Circuit of HWR, when node A is positive w.r.t node B
Notes: Fig 8: Voltage at node A is positive with respect to voltage at node B, forces the diode to be forward bias and act as a short. This results in current flow through the load resistance RL. Hence output voltage is approximately equal to the secondary voltage.
fig. 9: during the negative half cycle, the voltage at node A is negative with respect to node B that forces the diode in reverse biased and act as open circuit. This results in no current flow through the load

## Slide 12: Working of HWR
Equivalent Circuit of HWR, when node A is negative w.r.t node B

## Slide 13: HWR Waveforms
Ideal Diode
Practical Diode

## Slide 14: Performance parameters of HWR
DC/average output voltage
Ripple factor
Efficiency
Peak inverse voltage(PIV)

## Slide 15: Performance parameters of HWR
= ≃

## Slide 16: Average/DC value of load current ()
=d
= sin () d
=
=

## Slide 17: Average/DC voltage across the load ()
= *
= *
= *
=

## Slide 18: RMS value of load current ()
= in general
=
= =
=

## Slide 19: RMS value of the load voltage ()
= *
= *
= *
=

## Slide 20: Ripple factor (ϒ)
ϒ=
ϒ = = 1.21 independent of load current and input voltage

## Slide 21: Efficiency (η)
η =
= = *
= = *
η = =
If diode is ideal, η= 40.6%

## Slide 22: Peak Inverse Voltage(PIV)
Peak inverse voltage (PIV) is the maximum voltage which appears across the diode when it is reverse biased.
Choose a diode such that the breakdown voltage of the diode is greater than PIV, otherwise the diode will get damaged.
For HWR choose a diode with PIV rating>

## Slide 23: Topics covered in last class
Need of AC to DC conversion
Block diagram of DC power supply unit
Introduction to Rectifiers
Working of half wave rectifier
Performance analysis of half wave rectifier

## Slide 24: Numerical Problems
Q1. A voltage v = 100 Sin ωt and frequency 50 Hz is applied to half wave rectifier. If the load resistance is 2KΩ , calculate:
  Peak value of load current
  Average load current
  Rms or effective load current
  Average output voltage, Rms output voltage
  AC input power, DC output power
  Efficiency
  Ripple factor
  Ans: Vm=100V, (a) 50mA, (b)15.9mA, (c) 25mA (d) 31.8V , 50V (e) 1.25W, 0.50562W (f) 0.404 (g) 1.21

## Slide 25
Q2. An AC input of 230V,50Hz is applied to a transformer having turns ratio 10:1. Secondary of the transformer is connected to a HWR. Find all the performance parameters of the rectifier. = 1kΩ
RMS voltage at the primary of transformer= 230V
Turns ratio= 10:1
RMS voltage at the secondary of transformer= 23V
Input to the rectifier =sin (ωt)
= 32.52V

## Slide 26
= = 32.52mA
Average/DC value of load current = = 10.35mA
Average/DC voltage across the load = = 10.35V
RMS value of load current = = 16.25mA
RMS value of the load voltage = = 16.25V
Ripple factor ϒ = = 1.21
Efficiency η= 40.6%
PIV > : PIV >32.52V

## Slide 27
Q3. A sinusoidal voltage of peak value 10V is applied to a HWR. If the load resistance is 800Ω, calculate all the performance parameters of the rectifier.

## Slide 28: Full Wave Rectifier with centre tapped transformer

## Slide 29: Full Wave Rectifier with centre tapped transformer

## Slide 30: Working of Full Wave Bridge Rectifier
Center tapped FWR for node A is positive w.r.t B

## Slide 31: Working of Full Wave Bridge Rectifier
Center tapped FWR for node B is positive w.r.t A

## Slide 32
Note: Current through load during both cycles is in same direction (from node C to ground)
The frequency of the output signal =Twice the input frequency

## Slide 33: Performance parameters of FWR
= sin ()
Where is the peak value of the input current
= = (Assume ideal diode with = 0 ; =0)

## Slide 34: Average/DC value of load current ()
=d()
= sin ()d()
=
=

## Slide 35: Average/DC voltage across the load ()
= *
= *
= *
=

## Slide 36: RMS value of load current ()
=
=
= =
=

## Slide 37: RMS value of the load voltage ()
= *
=*
= *
=

## Slide 38: Ripple factor (ϒ)
ϒ= =
ϒ= =
ϒ = = 0.483 independent of load current and input voltage

## Slide 39: Efficiency (η)
η =
= = *
= = *
η = =
If diode is ideal, η= 81%

## Slide 40: Peak Inverse Voltage(PIV)
Maximum voltage across the diode when it is reverse biased
Choose a diode with PIV>

## Slide 41
Q4. A sinusoidal voltage of = 20 sin (2π*50*t) is applied to a FWR. If
= 1kΩ, calculate all the performance parameters.
Input to the rectifier = 20 sin (2π*50*t)
= 20V

## Slide 42
= = 20mA
Average/DC value of load current = = 12.73mA
Average/DC voltage across the load = = 12.73V
RMS value of load current = = 14.142mA
RMS value of the load voltage = = 14.142V
Ripple factor ϒ = = 0.483
Efficiency η= 80.12%
PIV > : PIV >40V

## Slide 43: Q4. A center-tapped FWR is supplied with 230V, 50 Hz AC mains through a step down transformer with turns ratio equal to 10. If = 1kΩ, find the average and RMS value of the load current, PIV rating of the diode used for proper working.
Ans: Vm=16.26V, Im=16.26mA, Iav=10.35mA, Irms =11.49mA, PIV>32.52V

## Slide 44: Q5. A sinusoidal voltage with 20-0-20 V applied to secondary of the transformer used for full wave rectification. If the load resistance is 1000Ω, calculate : (a) Peak value of load current (b) Average load current (c) Rms load current (d) Average output voltage (e) Rms output voltage (f) Efficiency (g) Ripple factor
Ans: Vm=28.28V, Im=27.4mA, Idc=17.44mA, Irms=19.3mA, Vrms=19.37V, Vdc=17.44V, Eff=80%, Ripple factor=0.483

## Slide 45: Bridge Rectifier
Fig.17(a) : Bridge FWR

## Slide 46: Working of Bridge FWR
Bridge FWR when node A is positive w.r.t B
Notes: For the first half of the time period, during which node A is positive with respect to B, D1 and D2 are forward biased whereas D3 and D4 are reverse biased. As said earlier considering ideal diodes D1, D2 are shorted and D3,D4 are open as in fig 18. This results in a current flow taking a closed path from node A, through D1, R-Load, D2 and from node B through the secondary coil as indicated. Note that current through the load resistor flows from node C to ground.
Similarly for the second half of the time period, during which node B is positive with respect to A, D3 and D4 are forward biased whereas D1 and D2 are reverse biased. Diodes D3, D4 are shorted and D1,D2 are open as shown in figure 19. This results in a current flow taking a closed path from node B, through D4, R-Load, D3 and from node A through the secondary coil as indicated. Note that again current through the load resistor flows from node C to ground even though the current through the secondary has reversed.
Thus output voltage is unidirectional for both the half cycle

## Slide 47: Working of Bridge FWR
Bridge FWR when node B is positive w.r.t. A
Note: Current through load for both cycles is in same direction
(from node C to ground)

## Slide 48: Bridge FWR
Fig. 20 : Input and output waveforms of bridge rectifier
Note: The frequency of the output signal =2 times the input frequency

## Slide 49
PIV : Vm , where Vm peak of secondary voltage (between node A and node B).
Other parameters same as Center tapped FWR:
Ripple factor is:
Efficiency:
Bridge FWR

## Slide 50
Comparison of Rectifiers
Parameters of rectified signal | HWR | Center-tapped FWR | Bridge FWR
Vdc |  |  | 
VRMS |  |  | 
PIV |  |  | 
Ripple factor |  |  | 
Efficiency |  |  | 
Frequency fo |  |  | 
1.21 0.483 0.483
40.6% 81.2% 81.2%

## Slide 51
Advantages of HWR over FWR
Advantages of Center tapped FWR rectifier over HWR
Advantages of bridge rectifier over to centre-tap FWR
Comparison of Rectifiers
Disadvantages of HWR over FWR
Disadvantages of centre-tap FWR over Bridge
Disadvantages of bridge rectifier over other rectifiers
Notes: Advantages of HWR over FWR
Simple circuit
Single diode
PIV rating is Vm
Advantages of Center tapped FWR rectifier over HWR
High Efficiency
low ripple factor
Advantages of bridge rectifier over to centre-tap FWR
PIV rating is Vm
Does not use Centre-tap transformer
Disadvantages of HWR over FWR
High ripple factor
Low efficiency
Disadvantages of centre-tap FWR over Bridge
Uses center tapped transformer
Disadvantages of bridge rectifier over other rectifiers
Four diodes are used

## Slide 52
Capacitor Filter
Commonly referred as C type filter
Key component of filter is the energy storing elements. Example: Capacitor
Capacitor allows AC component and blocks DC component
Capacitor helps to hold the output voltage to its maximum or peak value.
It can be used with HWR as well as with FWR

## Slide 53
Capacitor Filter
C type filter with HWR
Notes: The property of a capacitor is that, it allows ac component and blocks dc component. The operation of the capacitor filter is to minimize the ripple and to increase the dc voltage.

## Slide 54
Capacitor Filter
Fig: C type filter with Bridge FWR

## Slide 55
Capacitor Filter
Fig. 23 Filtered output waveform using C type filter
Notes: The capacitor charges to its peak value through Diode and secondary. But as the voltage starts reducing from peak value the Capacitor tries to retain the voltage to the peak. But the capacitor will discharge through the load resistance slowly until the transformer secondary voltage again increases to a value greater than the capacitor voltage.

## Slide 56
Ripple factor with Capacitor Filter
For HWR
For FWR

## Slide 57
Ripple factor with Capacitor Filter
DC value of filtered output for HWR
Note: here f is the frequency of the input signal
DC value of filtered output for FWR

## Slide 58
Comparison of Rectifiers
Parameters of rectified signal | HWR | FWR
Vdc |  | 
Ripple factor |  | 

## Slide 59: Numerical Problems
  1. Primary voltage is 120V, 60Hz. Turns ratio is 5:1. This transformer supplies to bridge rectifier employing 4 identical ideal diodes. The load resistance is 1kΩ. Calculate average and rms load voltage, efficiency, ripple factor, PIV rating and frequency of output waveform.
Ans: Vm=33.9V, Im=33.9mA, PIV>33.9V Vdc=21.58V, Vrms= 24V

## Slide 60
  2. A half wave rectifier with capacitor filter is supplied from transformer having peak secondary voltage 20V and freq 50Hz. The load resistance is 560Ω and capacitor used is 1000μF. Calculate ripple factor and dc output voltage. Draw the filtered output and label peak and dc value.
  (Ans:0.0103, 19.65V)

## Slide 61
  3. A full wave rectifier with capacitor filter has to supply an average voltage of 30V to 900Ω load. Calculate the rms input voltage and value of capacitor such that the ripple factor does not exceed 0.05, assuming f = 50Hz.
  Ans: C>64.15microF, Vm=32.59V, Vrms=23V

## Slide 62
4. (a) A half wave rectifier is fed from a transformer having turns ratio 6:1.The primary voltage is 110V at 60Hz. It is decided to have ripple factor of 0.03 and dc load current of 500mA. Find the value of capacitor needed. (b) Repeat for full wave bridge rectifier
Ans: C=3.25mF

## Slide 63
5. A load is to be supplied 10mA current at 5V dc, with ripple not more than 0.2%. Calculate the value of capacitor needed for the full wave bridge rectifier. Also, if the primary voltage of transformer is 220V at 50Hz, calculate the turns ratio needed.
(Ans: 2.89mF, 62)

## Slide 64: Summary
Discuss block diagram of a basic DC power supply unit.
Explain and analyze the working of various rectifier circuits.
Evaluate Output DC value, ripple factor, efficiency and PIV, of different rectifier circuits.
Explain the working of rectifier circuits with capacitor filter