## Slide 1: Part – I : ANALOG ELECTRONICS
CHAPTER-1: DIODES AND APPLICATONS
Module – 3: Voltage Regulators
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012

## Slide 2: Module – 3: Voltage Regulators
Learning Outcomes:
At the end of this module, students will be able to:
Zener diode and its V-I characteristics
Describe the working of Zener as voltage regulator

## Slide 3: Block diagram of a DC power supply

## Slide 4: Zener Diodes
Heavily doped diodes
Used in voltage regulators
Acts like regular diode-forward biasing
Under reverse bias, increase in voltage after Vz causes current to increase sharply maintaining voltage constant
Rated according to the voltage at which they will turn ON or begin to conduct reverse current

## Slide 5: Zener Diode and its characteristics
Anode
Cathode
P
N
P
N
IZK or IZmin
IZM or IZMax
PZM or PZMax
PZM = VZ.IZM
Notes: Zener diode:
Zener diode (also referred as regulated diode) is a two terminal device that is widely used in voltage regulators. When the reverse bias, applied to the semiconductor, has reached to zener voltage Vz , the current will be dramatically increased while the voltage keeps constant.
IZK or IZmin – Minimum current necessary to maintain breakdown
IZM or IZMax – Maximum current that can be safely passed through the zener diode
PZM or PZMax – Maximum power dissipation across zener diode
PZM = VZ.IZM
Zener diode is always connected such that it is reverse biased, and it is in zener breakdown region

## Slide 6: Equivalent circuit of Zener Diode
Equivalent circuits of Zener diode
Forward Reverse Breakdown
Note: RZ is usually very small, can be neglected

## Slide 7: Zener voltage regulation
Notes: Zener diodes are widely used to regulate the voltage across a circuit. When connected in parallel with a variable voltage source so that it is reverse biased, a zener diode conducts when the voltage reaches the diode's reverse breakdown voltage. From that point it keeps the voltage at that value.

## Slide 8: Working of Zener Diode : Vi and R fixed
Determine state of the diode
Use appropriate equivalent circuit
Basic Zener Regulator

## Slide 9: Working of Zener Diode : Vi and R fixed
Determine state of the diode
If Zener diode is ON
If the diode is OFF

## Slide 10: Working of Zener Diode : Vi and R fixed
Equivalent Circuit for ON condition
(Zener Current)
=
(Power dissipated in Zener diode)

## Slide 11: Line Regulation
Fixed and variable

## Slide 12: Load Regulation
Fixed Vi and variable RL

## Slide 13: Numerical Problems
For the zener network, Vi= 16 V, RS= 1 K, VZ= 10 V and RL= 1.2 K. Determine Vo, IZ and PZ
Repeat with RL= 3 K
(Ans:: 8.73 V, 0, 0)( 10V, 2.67mA, 26.7mW)

## Slide 14
3. In a zener network, RS = 120Ω, RL = 250Ω and VZ = 5V. Find the minimum and maximum current flowing through zener when input varies from 9V to 15V.
(Ans: 13.33mA, 63.33mA)

## Slide 15
4. For the Zener network shown, RS = 10Ω, VZ = 10V, Vi = 25V. Find the minimum and maximum current through Zener when RL is varied between 10Ω and 100Ω
Ans: (0.5A,1.4A)

## Slide 16
For a zener network, RS = 470Ω, VZ = 12V and Vi = 50V. Find the minimum and maximum values of RL so that Zener diode remains in ON state, given that IZK = 2 mA and PZM =500mW
(Ans: 152 -306 ohms)

## Slide 17
6. In a Zener regulator, the input DC is 10 V ± 20%. The output requirements are 5 V, 20 mA. Given Izmin=5 mA and Izmax=80 mA. Design the Zener regulator.
( Ans: RL=250 Ω, Vinmin=8V , Vinmax=12 V, Rmax=120 Ω , Rmin=70 Ω.)

## Slide 18
7. (a) Consider the circuit shown below.
The Zener Diode regulates at 50V over a range of diode current from 5 mA to 40 mA. Supply voltage V = 200V. Calculate the value of R to allow voltage regulation from a load current IL = 0 upto Imax; the maximum possible value of IL. What is Imax? (Ans: Imax=35 mA)
(b) If R is set as in part (a) and IL = 25mA, what are the limits between which V may vary without loss of regulation in the circuit?
(Ans: Vmin=162.5 V, Vmax=293.8 V )