## Slide 1: Part – I : Analog Electronics
Chapter-2: BJT and its Applications
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012
MODULE 1: BJT Characteristics

## Slide 2: BIPOLAR JUNCTION TRANSISTOR
Objectives
Discuss the operation of BJT.
Draw CB and CE configuration of transistor.
Explain input and output characteristics of CB and CE Configurations of transistor.
Derive expressions for current gains in transistor.

## Slide 3: INTRODUCTION
IMAGES OF TRANSISTOR
( Courtesy : wikipedia.org )
BJT is 3 layer/terminal semiconductor device
Used in signal amplifiers, switches and oscillators
Notes: Invented by a team of scientists at Bell laboratories during 1947-48.
Advantages of Transistors
  Small size and light weight
  Low power consumption and operating voltages
  Low price

## Slide 4: INTRODUCTION
Two types of transistors: NPN and PNP
The three layers of BJT are called Emitter, Base and Collector
Base is lightly doped. Emitter is heavily doped. Collector is moderately doped
BJT has two junctions – Emitter-Base (EB) Junction and Collector-Base (CB) Junction.
Notes: The device is called “bipolar junction transistor” because current is due to motion of two types of charge carriers – free electrons & holes.

## Slide 5: INTRODUCTION
Transistor symbols:
NPN Transistor PNP Transistor

## Slide 6: Transistor Operation
Depending upon the bias condition (forward or reverse) of each of the two junctions, different regions of operation for the BJT are obtained
Active region- transistor operating as an amplifier (linear region)
Saturation & cutoff region- Switching applications, e.g. in logic circuits
Region

## Slide 7: NPN TRANSISTOR OPERATION
http://www.learnabout-electronics.org/bipolar_junction_transistors_05.php
Operation of NPN transistor and PNP is similar with roles of free electrons and holes interchanged
Notes: Operation of PNP is similar with roles of free electrons and holes interchanged.

## Slide 8: CURRENTS IN TRANSISTOR
For both NPN and PNP transistor:
Collector current:
  : Current due to injected charge carriers from
  emitter
  : Current due to thermally generated minority
  carriers
Notes: Value of αdc < 1, since IE>IC

## Slide 9: TRANSISTOR CONFIGURATIONS
BJT has three terminals
Accordingly three configurations exist:
  Common Base (CB) configuration
  Common Emitter (CE) configuration
  Common Collector (CC) configuration
    (The last one is not discussed in this course)

## Slide 10: COMMON BASE CONFIGURATION
Base is common between input and output terminals

## Slide 11: CURRENTS IN TRANSISTOR
For both NPN and PNP transistor:
Collector current:
  : Current due to injected charge carriers from
  emitter
  : Current due to thermally generated minority
  carriers
Neglecting reverse saturation current ICBO ,
αdc : Common-base dc current gain
Notes: Value of αdc < 1, since IE>IC

## Slide 12: Numerical Problems
2. A transistor with α = 0.98 and ICBO = 5 µA has IB = 100 µA. Find IC and IE. (Ans: 5.15 mA, 5.25 mA)
1. In a transistor, 99% of the carriers injected into the base cross over to the collector region. If collector current is 4mA and collector leakage current is 6 μA, Calculate emitter and base currents. (Ans: 4.034 mA, 34μA)

## Slide 13: CB CONFIGURATION INPUT CHARACTERISTICS
CB Input characteristics
  A plot of input current(IE) versus input voltage (VBE ) for various values of output voltage (VCB)

## Slide 14: Base Width modulation
As the reverse bias voltage VCB is increased, the depletion region width at the C-B junction increases and base width decreases. Hence number of electron-hole combination at the base decreases. So base current reduces. Emitter current increases due to increase in concentration gradient (because of reduced effective base width).
This phenomenon is also called as the Early effect

## Slide 15: CB CONFIGURATION INPUT CHARACTERISTICS
CB Input characteristics
  A plot of IE versus VBE for various values of VCB.

## Slide 16: CB CONFIGURATION OUTPUT CHARACTERISTICS
  A plot of output current IC versus output voltage VCB for various values of input current IE .
Notes: Active region: E-B junction is forward biased and C-B junction is reverse biased.
Saturation region: E-B junction forward biased and C-B junction is forward biased.
Cut-off region: E-B junction is reverse biased and C-B junction is reverse biased.

## Slide 17: CB CONFIGURATION OUTPUT CHARACTERISTICS
  A plot of IC versus VCB for various values of IE .
    Divided into three regions:
      Active Region
      Saturation Region
      Cutoff Region
Notes: Active region: E-B junction is forward biased and C-B junction is reverse biased.
Saturation region: E-B junction forward biased and C-B junction is forward biased.
Cut-off region: E-B junction is reverse biased and C-B junction is reverse biased.

## Slide 18: COMMON EMITTER CONFIGURATION
Emitter is common between input and output terminals

## Slide 19
CURRENTS IN TRANSISTOR

## Slide 20: CURRENTS IN TRANSISTOR
βdc : Common emitter dc current gain
Reverse saturation current in CE configuration
  Note ICEO >> ICBO
Notes: Β>1, since IB < IC

## Slide 21: Relation between alpha and beta

## Slide 22: CE CONFIGURATION INPUT CHARACTERISTICS
Plot of IB versus VBE for various values of VCE

## Slide 23: CE CONFIGURATION OUTPUT CHARACTERISTICS
  A plot of IC versus VCE for various values of IB .
    Divided into three regions:
      Active Region
      Saturation Region
      Cutoff Region

## Slide 24: Exercise Problems
An NPN transistor has collector current 4mA and base current 10 μA. Calculate the alpha and beta values of the transistor, neglecting the reverse saturation current ICBO. (Ans: 0.9975, 400)
2. In a transistor circuit, when the base current is increased from 0.32 mA to 0.48 mA, the emitter current increases from 15 mA to 20 mA. Find αac and βac values.
(Ans: 0.968, 30.25)
3. A Ge Transistor has collector current of 51 mA when the base current is 0.4 mA. If β = 125, then what is its collector cutoff current ICEO?
(Ans: 1 mA)
4. The reverse leakage current of the transistor, when connected in common base mode is 0.1 μA, while it is 16 μA when the same transistor is connected in common emitter mode. Find αac and βac
(Ans: 0.993, 159)

## Slide 25: Summary
In this module we have learnt:
The operation of a transistor and the relevant current components.
To plot the input and output characteristics of CB and CE Configuration transistor.
To find current gains in different configurations of transistor.

## Slide 26: Part – I : Analog Electronics
Chapter-2: BJT and its Applications
Module 2: Transistor Biasing
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012

## Slide 27: Module 2: Transistor Biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
Objectives
Discuss the concept of biasing of the transistor.
Analyse the fixed and self bias circuits.
Identify the circuit parameters that effect Q point.

## Slide 28: Biasing
Applying external dc voltages to ensure that transistor operates in the desired region.
Transistor circuit in CE Configuration
Applying KVL collector loop
Coordinates of load line
VCE =VCC ; IC = 0 mA
VCE =0 ; IC = VCC/RC

## Slide 29: Load line and Operating point
Notes: Operating Point: Intersection of load line with the base current results in operating point or Q point.

## Slide 30: Load line and Operating point
Variation in load
line with circuit
parameters VCC,
RC and RB

## Slide 31: Load line and Operating point
With reference to the graphs, with everything else held constant
  If RB is increased, transistor goes towards cut-off and if RB is decreased, transistor goes towards saturation
  If RC is increased, transistor goes towards saturation and if RC is decreased, transistor goes towards active region
  If VCC is increased, transistor goes towards active region and if VCC is decreased, transistor goes towards saturation

## Slide 32: Types of Biasing
Two types
  Fixed bias
  Voltage divider bias (self bias)

## Slide 33: Transistor biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
  Fixed bias
Notes:   The value of IB is “fixed” by choosing proper value for RB.

## Slide 34: Exercise Problems
Department of Electronics and Communication Engineering, MIT, Manipal
2
For a fixed bias circuit using Si transistor has RB = 500 kΩ , RC = 2 kΩ , VCC = 15V, β = 70. Find the collector current IC , VCE (Ans: 2.002mA, 10.996V)
2. A Si transistor is biased for a constant base current. If β = 80, VCEQ = 8 V, RC = 3 kΩ and VCC = 15 V, find ICQ and the value of RB required. ( Ans: 2.33mA, 493KΩ)
3. Repeat the above problem , if the transistor is a Germanium device. ( Ans: 2.33mA, 507KΩ)

## Slide 35: Transistor Biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
  2. Voltage divider bias (self bias)
Notes:   --Voltage-divider resistors R1 & R2 replace RB. of fixed bias.

## Slide 36: Transistor Biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
  2. Voltage divider bias (self bias)
Notes:   --Voltage-divider resistors R1 & R2 replace RB. of fixed bias.

## Slide 37: Transistor Biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
Equivalent circuit :
link\self bias.docx
Notes: Since IC is almost independent of β, Q-point is stable

## Slide 38: Exercise Problems
Department of Electronics and Communication Engineering, MIT, Manipal
2
For a self-bias circuit, the transistor is a Si device, RE = 200 Ω, R1 = 10R2 = 10 kΩ, RC = 2 kΩ, β = 100 and VCC = 15 V. Determine the values of ICQ and VCEQ.
( Ans: 3.13mA, 8.11V)
For a voltage divider bias circuit, the transistor is a Si device, RE = 400Ω, R1 = 56 kΩ, R2 = 12.2 kΩ, RC = 2 kΩ, β = 150 and VCC = 10 V. Determine the Q point. Also find VE, VB, VC
(Ans: 2.32mA, 4.426V)
For the voltage divider bias find IC,VE, VB and R1 . Given VCC = 18 V, VC =12V, R2 = 5.6 kΩ, RC = 4.7kΩ and RE =1.2 kΩ. Assume Si transistor with β = 75
For a self-bias circuit using silicon transistor, RE = 300 Ω, RC =500 Ω,
VCC = 15 V, β = 100 and β RE = 10R2. Find the values of R1 and R2 to get
VCEQ = VCC / 2.
(Ans: 9.03KΩ)

## Slide 39
For a self-bias circuit, the transistor is a Si device, RE = 200 Ω, R1 = 10R2 = 10 kΩ, RC = 2 kΩ, β = 100 and VCC = 15 V. Determine the values of ICQ and VCEQ.
( Ans: 3.13mA, 8.11V)

## Slide 40
For a voltage divider bias circuit, the transistor is a Si device, RE = 400Ω, R1 = 56 kΩ, R2 = 12.2 kΩ, RC = 2 kΩ, β = 150 and VCC = 10 V. Determine the Q point. Also find VE, VB, VC
(Ans: 2.32mA, 4.426V)

## Slide 41
For the voltage divider bias find IC,VE, VB and R1 . Given VCC = 18 V, VC =12V, R2 = 5.6 kΩ, RC = 4.7kΩ and RE =1.2 kΩ. Assume Si transistor with β = 75

## Slide 42
For a self-bias circuit using silicon transistor, RE = 300 Ω, RC =500 Ω, VCC = 15 V, β = 100 and β RE = 10R2. Find the values of R1 and R2 to get VCEQ = VCC / 2. (Ans: 9.03KΩ)

## Slide 43: Summary
In this module we have learnt:
Importance of biasing in transistors
Concept of load line, operating point and their significance
Operating point dependent on the circuit parameters such as supply voltage and resistor values as well as operating temperatures.
To analyse fixed bias circuit to obtain the operating point and plot the load line.
Finding the equivalent circuit for self bias circuit and analyse it to obtain the Q point.

## Slide 44: Part – I : Analog Electronics
Chapter-2: BJT and its Applications
Module 3: Transistor as an Amplifier
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012

## Slide 45: Module-3 : Transistor as an Amplifier
Objectives
Discuss the basic concepts of an amplifier.
Analyze the RC coupled amplifier circuit with and without feedback.
Plot the frequency response of an amplifier and define the bandwidth.

## Slide 46: Transistor Amplifier
Base current is the input
Collector current is the output
BJT amplifies the input current as long as it is biased in active region

## Slide 47: Transistor Amplifier
When Vin = 0 we get operating point IBQ, ICQ, VCEQ
As Vin varies iB, ic and VCE varies around IBQ, ICQ, VCEQ

## Slide 48: Transistor Amplifier

## Slide 49
Output voltage will be amplified version of but 180 degree out of phase w.r.t input
= = -
=-
When =0, =

## Slide 50: CE RC Coupled Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
Notes: CC is coupling capacitor (to block dc ), CE is emitter bypass capacitor (to prevent feedback).
R1 ,R2, ,RE ,RC are used for biasing

## Slide 51: RC Coupled Amplifier
R1, R2, Rc, RE used for biasing to select Q point
Capacitors are used for blocking DC
Cc coupling capacitor and CE emitter bypass capacitor

## Slide 52: RC Coupled Amplifier-Feedback
CE is present, No feedback
  Large gain
Without CE, there is feedback
  Gain reduces

## Slide 53: Frequency Response of RC coupled Amplifier
Frequency versus gain plot

## Slide 54: Frequency Response
Department of Electronics and Communication Engineering, MIT, Manipal
2
  Frequency response of amplifier:
  Low frequency, mid-band frequency and high frequency region
  Bandwidth of amplifier : fH - fL.
Notes:     Frequency response is a plot of gain versus frequency.
    3 dB frequency: The frequency were gain reduced by 3 dB of its maximum value.

## Slide 55: Transistor Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
  Frequency response of amplifier:
  Bandwidth of amplifier : fH - fL.
  link\freqency response.docx
Notes:     Frequency response is a plot of gain versus frequency.
    3 dB frequency: The frequency were gain reduced by 3 dB of its maximum value.

## Slide 56: Transistor Amplifier
Analysis of frequency response curve
  At very low frequencies, reactance of coupling capacitors is high, hence there is loss of signal voltage across capacitors, resulting in reduced gain
  Also at low frequencies, emitter bypass capacitor does not fully bypass the ac emitter current, hence more ac voltage drop develops across RE, resulting in reduced gain
  At very high frequencies, reactance of junction capacitances will become low. This offers low reactance path for signal to ground, thus reducing voltage gain.
  At mid frequencies, gain is maximum and constant

## Slide 57: Multistage Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
Gain in decibels,
(AV)dB = 20 log10 | AV |
Multistage transistor
Notes: Up to gain of 100 (i.e., 40 dB) is obtained with single transistor.
For larger gain, more amplifier stages are to be cascaded.

## Slide 58: 2 Stage RC Coupled Amplifier

## Slide 59
Q1.An amplifier is known to have a power gain of 40dB. If the output power is 4W, determine the input power. (Ans:0.4mW)

## Slide 60
Q2.What output power is obtained from an amplifier whose power gain is 55 dB, when the input power is 1 mW? (Ans: 316.23W)

## Slide 61
Q3. In a three-stage amplifier, the voltage gain of first stage is 40 dB, gain of second stage is 200 and that of third stage is 0 dB. Find the overall gain of the amplifier.(Ans: 86.02dB)

## Slide 62
4. A three-stage amplifier circuit has first stage gain of 45 dB, second stage gain of 50 dB and third stage gain of –5 dB. What is the overall gain? If input to the first stage is 0.1mV, what is the output of final stage? (Ans: 3.162V)

## Slide 63: Transistor as a switch

## Slide 64: Transistor as LED driver
Department of Electronics and Communication Engineering, MIT, Manipal
2
Notes: When Input voltage VIN is ZERO , transistor is OFF(cut-off region), LED is OFF..
When Input voltage VIN is HIGH , transistor is ON (saturation region) , LED turns ON.

## Slide 65: Transistor as Inverter
Notes: When A = 0 , transistor is OFF(cut-off region), Output Q = 1.
When A = 1, transistor is ON (saturation region) , Output Q = 0.