## Slide 1: PART II DIGITAL ELECTRONICS
Reference:
Malvino and Leach, Digital Principles & applications, 7th edition, TMH, 2010
Morris Mano, “Digital design”, Prentice Hall of India, Third Edition.
Chapter 4 : Codes

## Slide 2: Binary coded decimal codes
Weighted Codes

## Slide 3: Binary coded decimal codes
  Weighted binary codes are those binary codes which obey the positional weight principle.
  Each position of the number represents a specific weight.
  There exists a fixed weight associated with each bit position in the binary representation of the code character.
Weighted codes

## Slide 4: Binary coded decimal codes
Binary Coded Decimal code (BCD)
Consider the number (16.85)10
(16.85)10 = (0001 0110 . 1000 0101)

## Slide 5: Binary coded decimal codes
Non-Weighted Code is one in which the positions in the code do not have a specific weight. Examples are Excess-3. And Gray.
    EXCESS-3 CODE
    GRAY CODE

## Slide 6: Binary coded decimal codes
Decimal | BCD = 8421 | Excess-3 | Gray
0 | 0000 | 0011 | 0000
1 | 0001 | 0100 | 0001
2 | 0010 | 0101 | 0011
3 | 0011 | 0110 | 0010
4 | 0100 | 0111 | 0110
5 | 0101 | 1000 | 0111
6 | 0110 | 1001 | 0101
7 | 0111 | 1010 | 0100
8 | 1000 | 1011 | 1100
9 | 1001 | 1100 | 1101
Decimal to BCD, Excess-3 and Gray code

## Slide 7: Error Detection and Correction
Introduction
Single bit Error detection using parity bit
Single bit error correction using (7,4) Hamming code

## Slide 8: Error Detection Codes
Parity: Number of ones in the given code word.
Even & Odd parity:
Example: 0000 (1)odd-parity (0)even-parity
Example: 0100 (0)odd-parity (1)even-parity
Notes: Even parity: The parity bit is set to 0 or 1 at the transmitter in such a way that the total number of 1’s in the resulting code word (including the parity) bit is an even number.
Odd parity: The parity bit is set to 0 or 1 at the transmitter in such a way that the total number of 1’s in the resulting code word (including the parity bit) is an odd number.

## Slide 9: Error Correction code
Principle of error correction
Consider a (7,4) Hamming code
Let i1 i2 i3 i4 be information symbols
Let p1p2 p4 be check symbols
The parity equations:
p1 = i3  i5  i7
p2 = i3  i6  i7
p4 = i5  i6  i7

## Slide 10: Hamming Code
Can write the equations as follows (easy to remember)
p1 p2 i1 p4 i2 i3 i4
1 0 1 0 1 0 1
0 1 1 0 0 1 1
0 0 0 1 1 1 1
1 2 3 4 5 6 7
This encodes a 4-bit information word into a 7-bit code word
Notes: Properties of the code
  If there is no error, all parity equations will be satisfied
  Denote the outcomes of these equation checks as c1, c2, c4
  If there is exactly one error, then c1, c2, c4 point to the error
  The vector c1, c2, c4 is called syndrome
  The above (7,4) Hamming code is SEC code
The above method of construction can be generalized to construct an (n,k) Hamming code
Simple bound
  k = number of information bits
  r = number of check bits
  n = k + r = total number of bits
  n + 1 = number of single or fewer errors
  Each error (including no error) must have a distinct syndrome
  With r check bits max possible syndrome = 2r
  Hence: 2r  n + 1