## Slide 1: PART II DIGITAL ELECTRONICS
Reference:
Malvino and Leach, Digital Principles & applications, 7th edition, TMH, 2010
Morris Mano, “Digital design”, Prentice Hall of India, Third Edition.
Chapter 4 : Codes

## Slide 2: Binary coded decimal codes
Weighted Codes

## Slide 3: Binary coded decimal codes
  Weighted binary codes are those binary codes which obey the positional weight principle.
  Each position of the number represents a specific weight.
  There exists a fixed weight associated with each bit position in the binary representation of the code character.
Weighted codes

## Slide 4: Binary coded decimal codes
Binary Coded Decimal code (BCD)
Consider the number (16.85)10
(16.85)10 = (0001 0110 . 1000 0101)

## Slide 5: Binary coded decimal codes
Non-Weighted Code is one in which the positions in the code do not have a specific weight. Examples are Excess-3. And Gray.
    EXCESS-3 CODE
    GRAY CODE

## Slide 6: Binary coded decimal codes
Decimal | BCD = 8421 | Excess-3 | Gray
0 | 0000 | 0011 | 0000
1 | 0001 | 0100 | 0001
2 | 0010 | 0101 | 0011
3 | 0011 | 0110 | 0010
4 | 0100 | 0111 | 0110
5 | 0101 | 1000 | 0111
6 | 0110 | 1001 | 0101
7 | 0111 | 1010 | 0100
8 | 1000 | 1011 | 1100
9 | 1001 | 1100 | 1101
Decimal to BCD, Excess-3 and Gray code

## Slide 7: Error Detection and Correction
Introduction
Single bit Error detection using parity bit
Single bit error correction using (7,4) Hamming code

## Slide 8: Error Detection Codes
Parity: Number of ones in the given code word.
Even & Odd parity:
Example: 0000 (1)odd-parity (0)even-parity
Example: 0100 (0)odd-parity (1)even-parity
Notes: Even parity: The parity bit is set to 0 or 1 at the transmitter in such a way that the total number of 1’s in the resulting code word (including the parity) bit is an even number.
Odd parity: The parity bit is set to 0 or 1 at the transmitter in such a way that the total number of 1’s in the resulting code word (including the parity bit) is an odd number.

## Slide 9: Error Correction code
Principle of error correction
Consider a (7,4) Hamming code
Let i1 i2 i3 i4 be information symbols
Let p1p2 p4 be check symbols
The parity equations: (note: information bit (i) or data bit(D) both are same)
p1 = i3  i5  i7
p2 = i3  i6  i7
p4 = i5  i6  i7

## Slide 10: Error Detecting codes
When a binary data is transmitted and processed it is susceptible to noise that can alter or distort its contents.
The 1’s may be changed to 0’s and 0’s to 1’s.
These errors may cause serious problems so these errors must be detected and corrected.

## Slide 11: Parity
The simplest technic for detecting errors is that of adding extra bit known as parity bit to each word being transmitted.
The two types of parity are odd parity and even parity.
For odd parity the parity bit is set to zero or one at the transmitter such that total number of 1 bits in the word including the parity is odd number.( Example 1110000)
For even parity the parity bit is set to 0 or 1 at the transmitter such that the total number of 1 bit in the word including parity bit is an even number.(Example 1111000)

## Slide 12: Example
In an even parity scheme which of the following contain an error?
a)10101010
Ans: the number of 1’s are four which is even so no error.
b)10111001
Ans :the number of 1’s are five which is odd so error occurs.
Similarly solve for odd parity.

## Slide 13: Error correcting codes
A code is said to be an error correcting code if the correct code word can always be deduced from an erroneous word.
The 7 –bit hamming code has total number of 7bits out of 4 data bits and 3 are parity bits.
P1,P2,D3,P4,D5,D6,D7 ( Example1100110)
P are parity bits and D are data bits

## Slide 14
(P1,D3,D5,D7) (P2 ,D3,D6, D7) (P4,D5,D6,D7)
P1,P2,P4 are set to 0 or 1 so that it will establishes even parity over bits 1,3,5 ,7 and 2,3,6,7 and 4,5 6, 7

## Slide 15: Example
Encode data bits 1101 into 7 bit even parity hamming code?
P1,P2,D3,P4,D5, D6, D7
1 1 0 1
Bits(P1,D3,D5,D7) ie 1,3,5,7
P1 1 1 1 must have even parity but it is odd so P1 must be 1
Similarly Bits (P2, D3,D6,D7) is even so P2 =0
Bits (P4,D5,D6,D7) bits are even so P4 =0.
Therefore final code is 1010101

## Slide 16: Example
The message 1001001 coded in the 7 bit hamming code is transmitted through a noisy channel decode the message assuming that at most a single error occurred in each code word.
1,3,5,7 (1001) no error C1=0
2,3,6,7(0001) error C2 =1
4,5,6,7(1001) no error C3 =0
The error word C3C2C1 = 010 = 210 So complement the 2nd bit from left therefore correct code is 1101001

## Slide 17: Old question paper problem
Decode the message 01111110 using 7 bit hamming code.
1,3,5,7 is 0 1 1 0 no error therefore C1=0
2,3,6,7 is 1 1 1 0 error occurred therefore C2=1
4,5,6,7 is 1110 error occurred therefore C3=1
Error word C3C2 C1 = 110 = 6th bit error
Therefore corrected word Is 0111100

## Slide 18
END