## Slide 1: FUNDAMENTALS OF ANALOG COMMUNICATION

## Slide 2
What is Communication?
What are the different means of Communication?

## Slide 3: Basic Communication System

## Slide 4
→Info Source
→Input Transducer
→Transmitter
→Channel/ Medium
→Noise
→Receiver
→Output Transducer
→Destination

## Slide 5
Modulation:
Process of varying one or more properties of a periodic waveform, called the carrier signal, with a modulating signal that typically contains information to be transmitted.
Need for Modulation:
  1.To enable long distance communication
  Low frequency message; High frequency carrier
  2.To reduce the height of the antenna
  Antenna height is a function of wavelength λ
  λ inversely proportional to frequency; Lower frequency signal requires antenna of much height which is not practical
  3.For multiplexing
  A method by which multiple analog or digital signals are sent over a shared medium

## Slide 6: Classification of Modulation

## Slide 7: Amplitude Modulation
Process of varying the amplitude of the carrier wave proportional to the instantaneous amplitude of modulating signal(message signal)
Both Carrier and Message are analog
Modulating Signal(Message) + Carrier Signal = Amplitude Modulated Signal

## Slide 8: Waveforms

## Slide 9: AM Signal in detail
Message signal: m(t)= Cos (2πfmt) Carrier signal: c(t)= Ac Cos (2πfct)
AM signal s(t) = Cos (2πfct)
Where, , Ac the amplitude of message signal & carrier
fm fc the frequencies of message signal & carrier

## Slide 11: Modulation Index
  Decides the depth of modulation. Expressed as percentage
  →Under modulation when
  → Over modulation when
  → Perfect modulation when

## Slide 12: Effect of modulation index on AM wave
.
m=0.5
m=1.0
m=1.5

## Slide 13: Spectrum of an AM signal
= Ac Cos (2πfct ) + +
Sideband Amplitudes =
Bandwidth of AM =

## Slide 14: Power in an AM Wave
  + +
  + +
  = → =
  For 100% modulation, m=1
  = *1.5 → = *0.66
  Carrier power is 66% of the Total power in a perfectly modulated AM wave

## Slide 15: Modulation by several Sine waves
Let message signal/ modulating signal contain several sine waves
m(t)= Cos (2πfm1t) + Cos (2πfm2t) + …..+ Cos (2πfmnt)
Overall modulation index is given by =
=
Where , ,…. are the modulation index of individual sine waves

## Slide 16: Current Equation
=

## Slide 17: AM Detection

## Slide 18: Exercise 01
An audio signal of m(t)= Cos (2π 1000 t) amplitude modulates a carrier c(t)= Cos (2π 2000 t). Find
a)m b) c) d)Bandwidth e) when =1kΩ f)Amplitude of each side bands. Draw the frequency spectrum
Solution:
(t)= Ac Cos (2πfct)
= 40 Cos (2π 2000 t)
m= 0.25 ; = - = 1000 Hz ; = + = 3000 Hz
  = = = 0.825watts
  Bandwidth= 2= 2kHz

## Slide 19
Spectrum
40 volts
5 volts
5 volts
2 kHz
1 k Hz
3 kHz
BW= 2kHz

## Slide 20: Exercise 02
Certain AM transmitter radiates 10.125 kW of power when modulation index is 0.5. If two more sine waves corresponding to 40% and 60% modulation is transmitted simultaneously, determine the total power
Solution:
When only one sine wave corresponding to 50% modulation is present,
= → = → = 9kW
When 2 more sine waves corresponding m=0.4 and m=0.6 are present,
Overall modulation index = = 0.87
= 12.461kW

## Slide 21: Exercise 03
The antenna current of an AM transmitter is 8A when only carrier is transmitted, but increases to 8.93A when carrier is modulated by a single sine wave. Find the percentage modulation. Determine the antenna current when the depth of modulation changes to 0.8
Solution:
= → m= 70.1%
When m=0.8,
= 8 = 9.19 amp

## Slide 22: Exercise 04
When the modulation percentage is 75, an AM transmitter produces 10kW.How much of this is the carrier power? What would be the percentage power saving if the carrier and one of the sidebands were suppressed before transmission took place?
Solution:
  →= 7804 watts
  = = (10000-7804) / 2 = 1098watts
  If carrier and one of the sidebands were suppressed, saving in power= (7804+1098)/10k= 89.02%

## Slide 23: Exercise 05
When a broadcast AM transmitter is 50 percent modulated, its antenna current is 12A. What will the current be when the modulation depth is increased to 0.9?
Solution:
= → = 11.31A
When m=0.9,
= 13.4A

## Slide 24: Exercise 06
Sketch the AM wave
(t)= 10 Cos (12560t)
Solution:
Comparing with standard form of AM equation,
Ac=10 ; m=0.25 ; Am=2.5 ; fc=2kHz ; fm=1kHz

## Slide 26: Frequency Modulation
Process of altering the frequency of the carrier signal with respect to the instantaneous amplitude of the modulating signal.
Both Carrier and Message are analog
Modulating Signal(Message) + Carrier Signal = Frequency Modulated Signal

## Slide 27: FM Waveform

## Slide 28: Representation of FM Wave
f FM = fC + Kf m(t)
Kf is the frequency sensitivity, fC is the carrier frequency
m(t) is the modulating signal
      VFM (t) = AC cos[2fct + βsin (2fmt)] ,
where the modulation index
By Carson’s rule,
is the frequency deviation

## Slide 29: Exercise 01

## Slide 30: Exercise 02

## Slide 31: PULSE MODULATION TECHNIQUES

## Slide 32: Digital Transmission of Analog Data
Message Signal → Analog
Carrier Signal → Digital
Types
Pulse Amplitude Modulation (PAM)
Pulse Width Modulation (PWM)
Pulse Position Modulation (PPM)

## Slide 33: Pulse Amplitude Modulation(PAM)
Here the signal is sampled at regular intervals and each sample is made proportional to the amplitude of the message signal at the instant of sampling.

## Slide 34: PAM Waveform

## Slide 35: Pulse Width Modulation(PWM)
Here the amplitude and starting time of each pulse is fixed but the width of each pulse is made proportional to the amplitude of the modulating analog signal at that instant

## Slide 36: PWM Waveform

## Slide 37: Pulse Position Modulation(PPM)
Both the amplitude and the duration are kept constant while the position of each pulse in relation to the position of a recurrent reference pulse is varied by each instantaneous sampled value of the modulating signal
Note: Fixed amplitude & Fixed width pulse at every falling edge of PWM wave

## Slide 38: PPM Waveform

## Slide 39: Digital Modulation Techniques
Message Signal → Digital
Carrier Signal → Analog
Types
Amplitude Shift Keying (ASK)
Frequency Shift Keying (FSK)
Phase Shift Keying (PSK)

## Slide 40: Amplitude Shift Keying (ASK)
Amplitude of the carrier is changed in accordance with the binary information to be transmitted
Frequency and phase of the carrier are kept fixed.
Bit 1 is transmitted by a carrier of one particular amplitude. Bit 0 is transmitted by changing the amplitude to 0 Volt or no signal in this case.

## Slide 41: Waveform

## Slide 42: Frequency Shift Keying (FSK)
Frequency of the carrier is changed in accordance with the binary information.
One frequency for bit 1 and another frequency for bit 0.

## Slide 43: Waveform
.

## Slide 44: Phase Shift Keying (PSK)
Phase of the sinusoidal carrier is changed in accordance with the binary information.
Phase in this context is the starting angle at which the sinusoid starts.
To transmit bit 0, the phase of the sinusoid is shifted by 180o whereas to transmit bit 1, the phase of the sinusoidal carrier is shifted by another 180o.
Thus the carrier phase shift represents the change in the state of the information.

## Slide 45: Waveform