## Slide 1: Part –II
DIGITAL ELECTRONICS
Chapter -5: BOOLEAN ALGEBRA AND LOGIC GATES
Books :
Malvino and Leach, Digital Principles & applications, 7th edition, TMH, 2010
Morris Mano, “Digital design”, Prentice Hall of India ,Third Edition.

## Slide 2: Module – 1:Introduction to Boolean Algebra
Objectives
  At the end of this module, students will be able to:
    State the laws of Boolean algebra.
    Simplify Boolean expressions using Boolean Algebra theorems and postulates

## Slide 3: BOOLEAN ALGEBRA
Department of Electronics and Communication Engineering, MIT, Manipal
Introduction
Notes: Introduction :
Invented by George Boole in 1854
Also known as switching algebra.
It is the mathematical frame work to simplify and design digital logic circuit.
Used in synthesis & analysis of binary logical function.

## Slide 4: Basic Laws of Boolean algebra
Used to design and analyze logic circuit mathematically
Laws of union
  Law 1: A + 0 = A
  Law 2: A + 1 = 1
Laws of intersection
  Law 3: A . 1 = A
  Law 4: A . 0 = 0

## Slide 5: Basic Laws of Boolean algebra
Laws of tautology
  Law 5: A + A = A
  Law 6: A.A = A
Laws of complements
  Law 7: A + A’ = 1
  Law 8: A.A’ = 0
Law of double complement
  Law 9: A’’ = A

## Slide 6: Basic Laws of Boolean algebra
Laws of commutation
  Law 10: A + B = B + A
  Law 11: A.B = B.A
Laws of association
  Law 12: A+(B+C) = (A+B)+C
  Law 13: A.(BC) = (AB).C
Laws of distribution
  Law 14: A(B+C) = AB + AC
  Law 15: (A+B)(C+D) = AC + AD + BC + BD

## Slide 7: Basic Laws of Boolean algebra
Duality
  The Dual of any expression can be obtained easily by the following rules.
    1 Change all 0’s to 1’s
    2 Change all 1’s to 0’s
    3 AND’s (dot’s) are replaced by OR’s (plus)
    4 OR’s (plus) are replaced by AND’s (dot’s)
No. | Boolean Expression | Dual of the expression
1 | X + 0 = X | X . 1 = X
2 | X + Y = Y + X | X . Y = Y . X
3 | X + 1 = 1 | X . 0 = 0

## Slide 8: Basic Laws of Boolean algebra
Laws of absorption
  Law 16 : A (A + B) = A
  Law 17 : A + AB =A
  Law 18 : A (A’ + B) = AB
  Law 19 : AB + B’ = A+B’
  Law 20 : AB’ + B = A+B

## Slide 9: De Morgon’s Theorems
De Morgon’s First Theorem:
  It states that “the complement of product of variables is equal to sum of the complements of individual variable” i.e.
  Proof

## Slide 10: De Morgon’s Theorems
De Morgon’s Second Theorem:
  It states that compliment of sum of two variables is equal to product of compliment of two individual variables. i.e
  Proof

## Slide 11: Self Test
Why simplification is required?
Notes: Need for simplification
It will be always desirable to simplify any Boolean Expression to its simplest form before converting to a logic circuit so that the circuit is constructed with minimum number of logic gates. It makes cost effective and more reliable due to lesser number of interconnections.

## Slide 12: Example
  i) Simplify F = X’Y’Z + X’YZ
  ii) Prove that Y (WZ’ + WZ) +XY = Y(W+X)
Solution
  i) F = X’Y’Z + X’YZ
  = X’Z (Y’+Y) (Y’+Y=1)
  = X’Z

## Slide 13: Example
  L.H.S Y (WZ’ + WZ) +XY
  = YW(Z+Z’)+XY (Z+Z’=1)
  = YW + XY
  = Y(X+W)
  = R.H.S

## Slide 14: Exercise
Simplify the following
F = XY+XYZ+XYZ’+X’YZ (Ans : XY+YZ)
F = XYZ+X’Y+XYZ’ (Ans: Y)
Prove that (A+B) (A+C) = A+BC

## Slide 19: Summary
In this module we have learnt to:
  List the Boolean Algebraic theorems
  Need for simplification of Boolean Expression
  Simplify the given Boolean expressions by applying Boolean Algebraic theorems like De Morgon’s Theorem, Duality theorem, Laws of commutation etc.