## Slide 1: Types of Logical Circuits

## Slide 2
Combinational Circuits
→ Circuits whose present output depends on Present Input only
→ No feedback present
→ Examples: Adder circuits, subtractor circuits

## Slide 3
Sequential Circuits
→ Circuits whose present output depends on Present Input + Past output
→ There exist feedback
→ Possess memory
→ Examples: Flipflops, counters, shift registers

## Slide 4: Half Adder
→ A Combinational circuit that performs arithmetic addition of two bits
→ Two inputs are A&B
→ Outputs are Sum(S) and Carry(C)
→ While adding two bits ,
it would not consider carry from previous addition
A |  |  |  | 
 | 0 | 1 | 0 | 1
A |  |  |  | 
 | 0 | 1 | 0 | 1
B |  |  |  | 
 | 1 | 1 | 1 | 1
B |  |  |  | 
 | 1 | 1 | 1 | 1

## Slide 5
SUM= B + A = A⊕B
CARRY= AB
.
INPUTS |  | OUTPUTS | 
A | B | SUM(S) | CARRY(C)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 6: Implementation
Using Basic Gates Using XOR gate

## Slide 7: Full Adder
→ A Combinational circuit that performs arithmetic addition of two bits
along with carry from previous addition
→ Three inputs are A,B and
→ Outputs are Sum(S) and Carry out ()
→ While adding two bits , =1 is also considered (carry from addition of )
A |  |  |  | 
 | 0 | 1 | 0 | 1
A |  |  |  | 
 | 0 | 1 | 0 | 1
B |  |  |  | 
 | 1 | 1 | 1 | 1
B |  |  |  | 
 | 1 | 1 | 1 | 1

## Slide 8
.
INPUTS |  |  | OUTPUTS | 
A | B |  | SUM(S) | 
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
INPUTS |  |  | OUTPUTS | 
A | B |  | SUM(S) | 
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 9
SUM= + B + A + AB
= + A
= + A
= A
= B + A+ AB + AB
= B + A + AB = B + A+AB
= B + A
= B + A = B+ A + AB
= B + A = B +A
= AB + B + A

## Slide 10: Implementation

## Slide 11: Full adder using 2 HA and an additional gate

## Slide 12
SUM= A
= + AB
= + AB
= + + AB
= +
= + = + + A
= B+ A = B+ A
= AB + B + A

## Slide 13: Exercise
1.Implement a logical circuit to realize HALF SUBTRACTOR
Hint: Similar to HALF ADDER, Borrow is not considered
2.Implement a logical circuit to real FULL SUBTRACTOR
Hint: Similar to FULL ADDER, Borrow-in is considered
3.Implement FULL ADDER using basic gates

## Slide 14: FlipFlops
→ Sequential circuit
→ Basic 1 bit memory element
→ Has 2 stable output states and which are complementary to each other
→ Works upon the application of a Clock (CLK) signal

## Slide 15: Clock Signal (CLK)
CLK acts as a master control for flip flop working
Clock is usually a square wave/ repetitive train of pulses
One clock pulse Edges and levels of clock
Positive edges
Negative edges
Positive pulses

## Slide 16
Two types of triggering/activation:
  pulse-triggered
  edge-triggered
Pulse-triggered (Level Triggered)
  latches
  ON = 1, OFF = 0
Edge-triggered
  flip-flops
  positive edge-triggered (ON = from 0 to 1; OFF = other time)
  negative edge-triggered (ON = from 1 to 0; OFF = other time)

## Slide 17
SR Flipflop (Set-Reset Flipflop)
D Flipflop (DataLatch Flipflop)
JK Flipflop
T Flipflop (Toggle Flipflop)

## Slide 18: Symbolic Representation of Edge-Triggered Flip-flops
S-R, D and J-K edge-triggered flip-flops. Note the “>” symbol at the clock input.

## Slide 19: SR Flipflop
Clock input act as a control button
S,R are the 2 inputs
, are the outputs
, should always be complementary to each other

## Slide 20: Working of SR Flipflop
Keeping S=1, R=0 , if CLK is applied(CLK=1),results in =1 , =0
We say Flipflop is SET
If we make inputs S=0, R=0 and apply CLK, outputs will maintain
=1 , =0 NO CHANGE STATE.
This property is called MEMORY
Circuit hold the output value even after the input is altered

## Slide 21: CONTD..
Keeping S=0, R=1 , if CLK is applied(CLK=1),results in =0 , =1
We say Flipflop is RE-SET
If we make inputs S=0, R=0 and apply CLK, outputs will maintain
=0 , =1 NO CHANGE STATE.
This property is called MEMORY
Circuit hold the output value even after the input is altered

## Slide 22: Summary
1.Load the input
2.Apply CLK pulse
3.Record the Output
→ If CLK is absent(CLK=0), circuit is inactive. Varying S,R would not affect the outputs , . Device holds on the previous outputs
→ Input S=1; R=1 should be avoided.

## Slide 23
1 | 1 | 0 | 0 | 1 | 1 | 0 | Set
1 | 1 | 0 | 1 | 0 | 1 | 0 | 
CLK | INPUTS |  | Previous Outputs |  | Present Outputs |  | State
 | S | R |  |  |  |  | 
CLK | INPUTS |  | Previous Outputs |  | Present Outputs |  | State
 | S | R |  |  |  |  | 
1 | 0 | 0 | 0 | 1 | 0 | 1 | No change / MEMORY
1 | 0 | 0 | 1 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 1 | 0 | 1 | Reset
1 | 0 | 1 | 1 | 0 | 0 | 1 | 
1 | 1 | 1 | 0 | 1 | 1 | 1 | Race around/Invalid
1 | 1 | 1 | 1 | 0 | 1 | 1 | 
0 | X | X | 0 | 1 | 0 | 1 | No change
0 | X | X | 1 | 0 | 1 | 0 | 

## Slide 25: D Flipflop
Avoids the Race-around condition in SR Flipflop.
D is the data latch input ; Clock input act as a control button
, are the outputs
, should always be complementary to each other

## Slide 26: Working of D Flipflop
Keeping D=1, if CLK is applied(CLK=1),results in =1 , =0
We say Flipflop is SET or data is latched onto the device.
Keeping D=0, if CLK is applied(CLK=1),results in =0 , =1
We say Flipflop is RE-SET or data is latched onto the device.
After loading the data, if CLK is removed(CLK=0), changes in D would not affect the outputs , . Device holds on the previous outputs

## Slide 27: Summary
1.Load the input
2.Apply CLK pulse
3.Record the Output
→ There is no Race-around condition.

## Slide 28
CLK | INPUT | Previous Outputs |  | Present Outputs |  | State
 | D |  |  |  |  | 
CLK | INPUT | Previous Outputs |  | Present Outputs |  | State
 | D |  |  |  |  | 
1 | 1 | 0 | 1 | 1 | 0 | SET
1 | 1 | 1 | 0 | 1 | 0 | 
1 | 0 | 0 | 1 | 0 | 1 | RESET
1 | 0 | 1 | 0 | 0 | 1 | 
0 | X | 0 | 1 | 0 | 1 | NO CHANGE
0 | X | 1 | 0 | 1 | 0 | 

## Slide 30: JK Flipflop
Clock input act as a control button
J,K are the 2 inputs
Working is same as that of SR except when J=1, K=1; output toggles

## Slide 31: Working of JK Flipflop
Keeping J=1, K=0 , if CLK is applied(CLK=1),results in =1 , =0
We say Flipflop is SET
If we make inputs J=0, K=0 and apply CLK, outputs will maintain
=1 , =0 NO CHANGE STATE.
This property is called MEMORY
Circuit hold the output value even after the input is altered

## Slide 32: CONTD..
Keeping J=0, K=1 , if CLK is applied(CLK=1),results in =0 , =1
We say Flipflop is RE-SET
If we make inputs J=0, K=0 and apply CLK, outputs will maintain
=0 , =1 NO CHANGE STATE.
This property is called MEMORY
Circuit hold the output value even after the input is altered

## Slide 33: Overall Working
1.Load the input
2.Apply CLK pulse
3.Record the Output
→ If CLK is absent(CLK=0), circuit is inactive. Varying J,K would not affect the outputs , . Device holds on the previous outputs
→ When input J=1; K=1 output TOGGLES

## Slide 34
1 | 1 | 0 | 0 | 1 | 1 | 0 | Set
1 | 1 | 0 | 1 | 0 | 1 | 0 | 
CLK | INPUTS |  | Previous Outputs |  | Present Outputs |  | State
 | J | K |  |  |  |  | 
CLK | INPUTS |  | Previous Outputs |  | Present Outputs |  | State
 | J | K |  |  |  |  | 
1 | 0 | 0 | 0 | 1 | 0 | 1 | No change / MEMORY
1 | 0 | 0 | 1 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 1 | 0 | 1 | Reset
1 | 0 | 1 | 1 | 0 | 0 | 1 | 
1 | 1 | 1 | 0 | 1 | 1 | 0 | Toggle
1 | 1 | 1 | 1 | 0 | 0 | 1 | 
0 | X | X | 0 | 1 | 0 | 1 | No change
0 | X | X | 1 | 0 | 1 | 0 | 

## Slide 36: T Flipflop
Modification to JK flipflop.
When T=1 , output TOGGLES upon application of CLK pulse.
When T=0 , Previous state is maintained.
This is useful in designing counters.

## Slide 37
CLK | INPUT | Previous Outputs |  | Present Outputs |  | State
 | T |  |  |  |  | 
CLK | INPUT | Previous Outputs |  | Present Outputs |  | State
 | T |  |  |  |  | 
1 | 1 | 0 | 1 | 1 | 0 | TOGGLE
1 | 1 | 1 | 0 | 0 | 1 | 
1 | 0 | 0 | 1 | 0 | 1 | No change / MEMORY
1 | 0 | 1 | 0 | 1 | 0 | 
0 | X | 0 | 1 | 0 | 1 | NO CHANGE
0 | X | 1 | 0 | 1 | 0 |