## Slide 1: Chapter 3: Operational Amplifiers
Module 1 : Basics of OpAmp
Reference: Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuits Theory, 11th Edition, PHI, 2012

## Slide 2: Objectives
Draw the block diagram of an OPAMP and briefly describe the functions.
List and define key parameters of an OPAMP.
Discuss OPAMP based amplifier topologies.
Design OPAMP based circuits for simple mathematical operations.

## Slide 3
An OpAmp is a very high gain direct coupled amplifier which can amplify signals over a wide range of frequencies.
Used to perform various operations on signals such as addition, subtraction, multiplication along with amplification. Hence the name

## Slide 6
Symbol of OpAmp
Pin detail of µA741 IC

## Slide 7: Open loop configuration
OpAmp is a differential amplifier
Amplifies difference between voltage at
Non-inverting pin and Inverting pin.
Vout= Ad(V1-V2)
Vout= Ad(Vid)
Where,
Ad = Differential Gain
V1 = Voltage at Non inverting terminal
V2 = Voltage at Inverting terminal

## Slide 8
If input is applied to Non-inverting pin and inverting pin is grounded,
Vout= Ad(V1) ; Non inverting amplifier
If input is applied to inverting pin and Non-inverting pin is grounded,
Vout= - Ad(V2) ; Inverting amplifer ;output will be out of phase wrt input
If inputs are applied to both the pins, output will be proportional to the difference between the inputs

## Slide 9
If V1=V2 , Vout =???
Vout= ACM ()
ACM = Common mode gain; ability of OpAmp to amplify signal common to both pins(noise)
Overall
Vout= Ad(V1-V2)+ ACM ()

## Slide 10
  Differential Signal – To be amplified; Infinite Ad
  Noise Signal – To be suppressed; least ACM
  Common Mode Rejection Ratio=(Ad / ACM)
  In decibels; CMRR= 20log(Ad / ACM)
  Ideally CMRR= ∞

## Slide 11: Ideal Voltage Transfer Characteristics

## Slide 12: Block Diagram of an OpAmp

## Slide 13
Input stage:
Function is to amplify the difference between the two input signals.
Provides high differential gain
Intermediate stage:
Input stage alone cannot provide high gain, an intermediate stage is used to provide the required additional voltage gain
Buffer and Level shifting stage:
Level shifting stage is used to eliminate the dc level. Buffer is a unity voltage gain amplifier usually used for impedance matching.
Output stage:
Contributes to the overall gain of the op-amp and also provides low output impedance.

## Slide 14: Characteristics of OpAmp
1.Differential mode gain Ad
Factor by which difference between the input signals is amplified by the OpAmp
2.Common mode gain ACM
Factor by which common mode input voltage is amplified by the OpAmp
3.Common mode rejection ratio (CMRR)
Measure of ability of OpAmp to reject the signal common to both the input pins (noise)

## Slide 15
4.Input Resistance(Ri)
Equivalent resistance measured between the 2 input terminals of the OpAmp
5.Output Resistance(Ro)
Resistance measured at output pin with respect to ground
6.Bandwidth
Range of frequencies over which gain is constant

## Slide 16
7. Input bias current(Iib)
Average of the currents in the input terminals when both the input voltages are zero
Iib = when ==0
8.Input offset current(Iio)
Algebraic difference between the currents in the input terminals when both the input voltages are zero
Iio = when ==0

## Slide 17
9.Input offset voltage(Vio)
The differential voltage that must be applied at the input terminals inorder to make the output voltage zero
10.Output offset voltage(Voo)
Output voltage when both input voltages are zero. This is due to input offset voltage
11. Slew rate
Maximum rate of change of output with respect to time. Slew rate has to be very high if the OpAmp has to operate at high frequencies

## Slide 18: Ideal and Practical Op-Amp characteristic values
 | Characteristics | Ideal | Practical
1 | Band width | ∞ | 1MHz
2 | Input resistance, Ri | ∞ | 2MΩ
3 | Output resistance. Ro | zero | 75Ω
4 | CMRR | ∞ | 90dB
5 | Slew rate | high | 0.5 V/μs
6 | Input offset voltage | 0 | 6mv (max)
7 | Input offset current | 0 | 200 nA (max)
8 | Differential mode output voltage gain Ad | ∞ | 50000
9 | Common mode output voltage gain Ac | 0 | 10

## Slide 19
Q1. An OpAmp has of 99999 and common mode rejection ratio of 55dB.If non inverting voltage is 250µV, and inverting voltage is 240µV, calculate the output voltage of the OpAmp.

## Slide 20
Q2. For an OpAmp when =0.5mV and= -0.5mV,output is 8V. For the same OpAmp when ==1mV, output is 12mV. Calculate the CMRR of the device.

## Slide 21
Q3.For an OpAmp =, CMRR=60dB. If non inverting voltage is 150µV and inverting voltage is 140µV, calculate the output voltage.

## Slide 22: Ideal OpAmp - Equivalent Circuit

## Slide 23: Practical OpAmp - Equivalent Circuit