## Slide 1: Relationship between modulus of elasticity and modulus of rigidity Relationship between E, G and K Application problems
LECTURE 20
Contents:
HOME

## Slide 2
Relationship between young’s modulus of elasticity (E) and modulus of rigidity (G) :-
B
A
D
τ
τ
a
a
45˚
A1
φ
φ
B1
C
H
Notes: Consider a square element ABCD of side ‘a’ subjected to pure shear‘τ’. DA'B'C is the deformed shape due to shear τ.
Drop a perpendicular AH to diagonal A'C.
Strain in the diagonal AC = τ /E – μ (- τ /E) [ σn= τ ]
= τ /E [ 1 + μ ] -----------(1)
Strain along the diagonal AC=(A'C–AC)/AC=(A'C–CH)/AC=A'H/AC
In Δle AA'H
Cos 45˚ = A'H/AA'
A'H= AA' × 1/√2
AC = √2 × AD ( AC = √ AD2 +AD2)
Strain along the diagonal AC = AA'/ (√2 × √2 × AD)=φ/2 ----(2)
Modulus of rigidity = G = τ /φ
φ = τ /G
Substituting in (2)
Strain along the diagonal AC = τ /2G -----------(3)
Equating (1) & (3)
τ /2G = τ /E[1+μ]

## Slide 3
Consider a square element ABCD of side ‘a’ subjected to pure shear‘τ’. DA'B'C is the deformed shape due to shear τ.
Drop a perpendicular AH to diagonal A'C.
Strain in the diagonal AC = τ /E – μ (- τ /E) [ σn= τ ]
= τ /E [ 1 + μ ] -----------(1)

## Slide 4
Strain along the diagonal AC=(A'C–AC)/AC=(A'C–CH)/AC=A'H/AC
In Δle AA'H
Cos 45˚ = A'H/AA'
A'H= AA' × 1/√2
AC = √2 × AD ( AC = √ AD2 +AD2)
Strain along the diagonal AC = AA'/ (√2 × √2 × AD)=φ/2 ----(2)
Modulus of rigidity = G = τ /φ
φ = τ /G
Substituting in (2)
Strain along the diagonal AC = τ /2G -----------(3)
Equating (1) & (3)
τ /2G = τ /E[1+μ]
E=2G(1+ μ)

## Slide 5
E = 9GK/(G+3K)
Relationship between E, G, and K:-
We have
E = 2G( 1+ μ) -----------(1)
E = 3K( 1-2μ) -----------(2)
Equating (1) & (2)
2G( 1+ μ) =3K( 1- 2μ)
2G + 2Gμ=3K- 6Kμ
μ= (3K- 2G) /(2G +6K)
Substituting in (1)
E = 2G[ 1+(3K – 2G)/ (2G+6K)]
E = 18GK/( 2G+6K)
Notes: We have
E = 2G( 1+ μ) -----------(1)
E = 3K( 1-2μ) -----------(2)
Equating (1) & (2)
2G( 1+ μ) =3K( 1- 2μ)
2G + 2Gμ=3K- 6Kμ
μ= (3K- 2G) /(2G +6K)
Substituting in (1)
E = 2G[ 1+(3K – 2G)/ (2G+6K)]
E = 18GK/( 2G+6K)

## Slide 6
N12.A circular rod of 100 mm dia and 500 mm length is subjected to a tensile force of 2000 kN. Determine the modulus of rigidity, bulk modulus and the change in volume, if the poisson’s ratio=0.3 and E=2x105 N/mm2.
Ans:
G=0.77x105 N/mm2
K=1.67x105 N/mm2
dv=1994.9 mm3

## Slide 7
N13. The modulus of rigidity of a material is 0.8 x 105 N/mm2 . When a 6 mm x 6 mm bar of this material is subjected to an axial pull of 3600 N, it was found that the lateral dimension of bar is changed to 5.9991 mm x 5.9991 mm.
Find μ and E.
Ans:
µ=0.32
E=2.105x105 N/mm2

## Slide 8
T1. Find the Young’s modulus of a brass rod of diameter 25 mm and of length 250 mm which is subjected to a tensile load of 75 kN when the extension of the rod is equal to 0.3 mm.
T2. The ultimate stress, for a hollow steel column which carries an axial load of 2.0 MN is 480 N/mm2. If the external diameter of the column is 200 mm, determine the internal diameter. Take factor of safety as 3.

## Slide 9
T3. A brass bar having cross section area of 900 mm2, is subjected to axial forces as shown below. The lengths of portion AB, BC and CD are 0.6 m, 0.8 m and 1.0 m respectively. Determine the total elongation of the bar. Take E = 100 GPa.
40 kN
20 kN
70 kN
10 kN
A
B
C
D

## Slide 10
T4. A tensile load of 80 kN is acting on a rod of diameter 80 mm and of length 8 m. A bore of diameter 60 mm is made centrally on the rod. To what length the rod should be bored so that the total extension will increase 25% under the same tensile load. Take E = 200 GPa.

## Slide 11
T5. A steel flat of thickness 16 mm tapers uniformly from 80 mm at one end to 50 mm at the other end in a length of 800 mm, If the flat is subjected to a load of 120 kN, find the extension of the flat. Also calculate the percentage error if average area is used for calculating its extension. Take E=2x105 Mpa

## Slide 12
T6. A two meter long steel bar is having uniform diameter of 40 mm for a length of 1 m, in the next 0.5 m its diameter gradually reduces to 20 mm and for remaining 0.5 m length diameter remains 20 mm uniform as shown in the figure. If a load of 150 kN is applied at the ends, find the stresses in each section of the bar and total extension of the bar. Take E = 200 GPa.

## Slide 13
T7. A tensile load of 50 kN is acting on rod of 50 mm diameter and length of 5m. Determine the length of a bore of 25mm that can be made central in the rod, if the total extension is not to exceed by 25 percent under the same tensile load. Take E = 2.05 x 105 N/mm2

## Slide 14
T8. Determine the magnitude of the load P necessary to produce zero net change in the length of the bar shown in the figure below. Take A=400 mm2.
Ans:
P=170 kN

## Slide 15
T9. For the bar shown below, determine diameter of the central portion and its length, if the total extension of the bar is 0.16 mm. Take E=200 GPa. Stress at central portion is limited to 140 N/mm2
HOME
Ans:
d=37.18mm
x=140.23mm

## Slide 16
T10. A tension test is carried out subjected on a mild steel tube of external diameter 18 mm and internal diameter 12 mm. An an axial load of 2 kN produces an extension of 3.36 x 10-3 mm on a length of 50 mm and a lateral contraction of 3.62 x 10-4 mm of outer diameter.
Determine E, μ,G and K.
Ans:
E=2.11x105 N/mm2
µ=0.3
G=81.15x103 N/mm2
K=175.42x103 N/mm2